        RADIO CONTROL DATA FILE FORMATS

Last update:07/23/23

# INTRODUCTION

RadioCtl for Linux utilizes a number of different input and output files. This document describes the formats of these files. Definitions of the various terms used, and the operation of the RadioCtl program are described in the RadioCtl-Operation manual.

# File Formats
There are three different file types in use in the program. The first is the data files. These contain frequencies, groups, systems and other settings for the radios. These files can be in several formats, and can reside anywhere on the user's computer system.

The second file type is the configuration file for the radios being used. This file defines the name, protocols and other important information about each radio available to RadioCtl It also provides some customization for some program defaults. There should only be one of these files residing in the user's HOME directory.

The third file type is used by the GUI program for saving and restoring various program settings. There is only one of these, and the user normally does not need to make changes to this file.

## Record Field Types
Fields specified for each record must conform to the type defined for that field. For example a Number field CANNOT contain letters. When the program reads a data file, it will ignore any record that contains the wrong type in a field.
Table 1: Field Types
type	description
Integer	Whole, positive number or 0
Decimal	Positive Number with (or without) a decimal point, or 0
Hex	A hexadecimal integer. Value contains only digits 0-9 and a,b,c,d,e,f. The case of the letters is not important (F2 is the same as f2.)
Character	Any single ASCII recognized character. / NOTE: Due to the way that the data files are parsed, a comma (',') or equal sign ('=) cannot be specified in a character field
String	Any combination of letters, numbers and punctuation. / 'cntrl' characters (other than carriage-return and line-feed) should be avoided, as they can interfere with the processing. / NOTE: Due to the way that the data files are parsed, a comma (',') or equal sign ('=') cannot be included in any string.
Binary	TRUE or FALSE. 1, T, True, Y, Yes, On, (not case sensitive) are all interpreted as TRUE. All other entries are interpreted as FALSE.
Frequency	A positive integer or decimal number. If Decimal point is included in the value, then the value is assumed to be in MHz. Otherwise the value is assumed to be in Hz. A frequency of 0 indicates an empty channel or ignored setting.
Mode	Modulation string. Valid values are AM, FM, FMn, FMw, FMn, CW, SSB, LSB, USB, AUTO. Additionally digital decode modulations can be specified. Those are D-Star, dPMR, NXDN-VN, NXDN-N, DCR, DMR and P25. The string is NOT case sensitive. Not all modulations are valid for all radios. The program may modify the modulation based on the current radio. If AUTO specified, the modulation will be set based on the frequency. Currently, only certain ICOM radios recognize the digital modulations. For all other radios, these will be translated to FMn.
Tgid	Trunked Group ID. Can be in format nn-xxx or nnnn (where 'n' & 'x' are numbers).
bitstring	A string made up of only 1's and 0's. Ex: 011010011
Coord	GPS coordinate. Can be a Decimal number, or DMS format (DD:MM:SS:direction) / For Decimal number, the sign indicates N,S,E or W. For DMS, the direction is NOT case sensitive.
hex	Hexadecimal characters (0-9,A-F). Letters can be lower or upper case. These are usually for ICOM addresses. ex: 2F same as 2f.
protocol	The name of a RadioCtl supported protocol. Currently the following protocol names are recognized: Uniden, ICOM, Kenwood, AOR8000, Bearcat

# Data Files
  These files contain frequencies, modulations and other parameters that may be sent to or read from the various supported radios. These files can be created and modified by the user, or they can be created by the RadioCtl program. Data files are loaded/saved using the Files menu item on the GUI, or a parameter on the command line version. All data files are standard ASCII, with each record terminated with a LF character (ASCII code 10). Files created with Windows text editors will also contain a CR (ASCII code 13) at the end of each line. This type of file is also acceptable to the program.

In order for a data file to be recognized by the RadioCtl program, the first record in the file MUST contain the characters: *radioctl . The '*' MUST start in the first column of this record. The characters can be lower, upper or mixed case. Any other characters after this identifier are ignored.

The file processing routines recognize a '*' or '#' at the beginning of a record as a comment. These records are ignored by the program. In addition, a '#' in a record indicates the end of data, and can be used for adding comments to a single line of data. The user can add full line or record comments as desired. Note that user comments may be lost if the program reads a file and then saves it again.

Comment records that have a ':' as the second character designate a TAG record. These are special records that are used for special purposes. If the comment record starts with '#:', then the record is used to define the order of fields in positional records.

Non-comment records are comma delimited fields. The first field of every non-comment record MUST contain the record type. If the record type is not recognized, the record will not be processed, and an error message will be displayed. Valid record types are described in the sections below. The record type specification is NOT case sensitive. The record type will indicate what variable ('key') each field is assigned to. If the record ends (or a '#' is encountered) before all fields have been specified, the rest of the fields will be assigned default values.

If the second field in the record contains a '=' the record will be processed in the form: key=value, key=value,... where 'key' is a valid field name and value will be assigned to that field name in the database record. Keys are NOT case sensitive. Any record key not specified, will be assigned the default value.
If the second field in the record does NOT contain a '=', then all fields will be assigned to the database record based on the position in the record.

In general, either format is acceptable for most record types. The positional format is easier to read, but harder to create. The key=value format is easier to create, but not as easy to locate specific values. The default output for most records is positional.

There ARE a couple of record types that ONLY understand the key=value format.

Important: Because of the way that data records are processed, no value for either record format can contain a comma (',') an equal sign ('=') or a hash-tag ('#'), as this characters have special meaning.

Every record loaded from a file is assigned a record index. For certain records, this number is initially determined by the 'index' value in the input file. A number of data records contain 'references' to other record indexes. These references are designed primarily for Uniden radios. If a reference is 0, or references an undefined record, then the record is referred to as an 'orphan' and cannot be stored in Uniden radio. If multiple files are loaded by the program, all valid index references are adjusted to match any changes to the record indexes made by the program.

In general, the references are:
      FREQ->GROUP->SYSTEM
     TFREQ->SITE->SYSTEM
     BPLAN->SITE->SYSTEM.

A few record types do NOT reference other records. They include record types that are settings for the program or the radio.

 The record structure has been designed to be as general as possible. Some fields/keys defined may be applicable only to specific radios. In general, the program will ignore fields that are not used by the current radio being controlled. Also note that a number of fields are not included in the GUI databases.
A number of record types contain a field named EXTRA. This field is used ONLY for the positional record format. This field contains specifications for keys that are used by a limited number of radios, and utilize values that are positive integers or 0. By utilizing this field, the number of positions in a record can be minimized. Values in this field are in the form: XXXn, where "XXX'" is a keyword and 'n' is a number 0 or greater. There must NOT be any spaces between the 'XXX' and the number. Multiple specifications can be included in the EXTRA field, with each specification separated by a blank. When the record is in KEYWORD=VALUE format, 'EXTRA' is not specified as a keyword. Instead, the individual keywords are used. As an example:

 positional record: FREQ, , , , SCANGRP1 RFGAIN2, ,
 Keyword/value record: FREQ,SCANGRP=1, RFGAIN=2, ,

Note that keywords in either record format are NOT case sensitive. The list of keywords that can be included in an EXTRA field follow the description of each record type.
Extra keys are NOT included in the GUI databases.
.

Notes on Uniden Quick-keys:
  Quick-key implementation on the BCD396, the BCD325P2 and the SDS200 are a bit different.
The BCD396 has 100 system quick-keys (1-100). Each group in a system can have a quick-key from 0 to 9.
The BCD325P2 has 100 system quick-keys (0-99). Each group in a system can have a quick-key from 0 to 9.
The SDS100 and SDS200 have 100 Favorites quick-keys (0-99) that select a favorites file for scanning. Each Favorite has up to 100 system quick-keys (0-99) that are unique for that Favorites list. Each System has up to 100 department (group) quick-keys (0-99) that are unique for that System.
For RadioCtl, 'departments' are called 'groups'.
For trunked systems, the BCD325P2 ignores the System quick-key setting and instead utilizes the quick-key defined in the SITE records.
The SDS100 and SDS200 treat quick-keys defined in SITE records as department keys.
The BCD396 does not have separate SITE records, so the SYSTEM quick-key is always used for both conventional and trunked systems.

### Comment records
   Comments start with a '*' or a '#'. These records are ignored for most processing by both the GUI and the command line program. However, comments that start with a '#' are treated specially.

If a valid record type is preceded with comment records that start with a '#', these records are kept with that record when the file is processed. The rules for '#' records are as follows:
- There must be a '#' in the first column
- There must be NO blank lines, or lines that start with a '*' before the line that contains the record type.

An example:
   # This is a comment line
   # This Comment will also be kept
   freq, 12,The Comments Above will be kept with this freq record, .....

If a comment record starts with '#:', then the record will define the fields for a positional record type. These comments are called FORMAT comments and are in the form:
      #:rectype:field1,field2,field3,...
where 'rectype' is the record type (FREQ, SYSTEM, etc) and each field specified is the keyword for each positional field. The record type, and the fields specified can be in Upper, Lower or Mixed case.
FORMAT comments allow the user to utilize files that may have been created with older versions of Radioctl.
Multiple FORMAT comments can be included in a single file. All records following the FORMAT comment will utilize that format for positional records until another FORMAT comment is encountered.
FORMAT comments do NOT affect records in KEYWORD=VALUE format.
WARNING: Adding (or changing) a FORMAT comment can cause strange results if the positional fields do NOT match the format fields!

### TAG Records
Tag records are special comments that can be inserted by the user. Tag records will be preserved when a data file is read and then re-written at the beginning of the file. Tag records are in the format
 *:tagname: some text
where 'tagname' is a pre-defined tag. Tag records MUST start in column 1 of the file. The tagname is NOT case sensitive. However it is recommended that it be in UPPER case for clarity. When a file with tags is updated, all tags (except for a few special ones) will be preserved.

Table 2: Tags
tag	description
*:SYSTEM:	Name of the system (usually as per RadioReference.com)
*:QUICKKEY:	Uniden Quickkey assignments for the system. Multiple Quickkey tags can be present if the file contains more than one system. / Note: This tag is generated by the RadioCtl write subroutine and is not preserved if the file is reprocessed.
*:START:	Start of multi-line comments. Comments following this tag will be copied to any updates to the file.
*:END:	End of multi-line comments.

### SYSTEM Records
SYSTEM records define a particular system. There should be at LEAST one SYSTEM record in every data file. Any SITE & GROUP records that do not reference a valid SYSTEM record, will be marked as orphans. Any FREQ or TFREQ records that reference orphaned SITE or GROUP records will also be marked as orphans.
Uniden radios have the ability to store SYSTEM records. All other radios do not. The RadioCtl GUI program makes use of SYSTEM records for various operations for all radios. The GUI will ignore any SYSTEM definitions for trunked systems.

Table 3: SYSTEM record
n	key	type	description
1	rectype	string	Record type. (SYSTEM) / Information about a given system. SITE, GROUP & FREQ records are associated with a SYSTEM record.
2	index	integer	System number index. This number MUST be unique for all SYSTEM records in the file, and must be greater than 0. / If this number is 0, then this record will be discarded.
3	service	string	Description of the system. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio.
4	valid	binary	If TRUE, the record is active. Indicates if RadioCtl will utilize this record for scanning/searching. If the record is stored in the radio, this determines the 'lockout' setting in the radio. / NOTE: The Uniden BCD325P2 ignores system lockout for trunked systems. For this radio, lockouts are determined by the individual SITE records.
5	systemtype	string	type of system. For the GUI program, and all radios EXCEPT Uniden, only 'CNV' (conventional) types are recognized. All other types are considered trunked systems, and only supported by Uniden radios. / Systemtype is NOT case sensitive. / Valid values for systemtype are: / systemtype Description / CNV Conventional system / LTR LTR trunked system / EDS EDACS Scat / EDW EDACS Wide / EDN EDACS Narrow / MOTS Motorola Standard / MOTP Motorola Sprinter / MOTC Motorola Custom (Needs BPLAN record) / TRBO Motorola Turbo (DMR) / DMR Single channel DMR / P25S P25 standard (Phase I or II) / P25F P25 single channel / P25X P25 X2 TDMA (SDS100/SDS200 only) / NXDN NXDN (SDS100/SDS200 only) / NXDNS NXDN Single Channel (SDS100/SDS200 only)
6	flags	character	Flags for the record. Each flag is a single character indicating a special characteristic of this record. Most of the flags affect Uniden Radios, and are not used by the RadioCtl GUI. / Flag characters can be upper or lower case. / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified as keyname=1 (where 'keyname' is the affected key). / Valid flag characters are: / character key meaning / A atten Attenuation is on for this system. / C call I_Call enabled (BCD396 only) / F afs TGID format is AFS (nn-xxx) / H agc_digital AGC Digital is on / I id_search ID-Search is On / J agc_analog AGC Analog is on / K skip Data Skip is on. (BCD396 only) / O c_ch Control Channel Only (BCD396 only) / Q qkeyon Turn on System quick key specified when writing to the radio. (BCD325P2 and BCD396 only). If set, any quick keys specified in SITE records for this system will also be turned on. / S s_bit Motorola status bit on / X moto_id P25 display in hex
7	dlyrsm	integer	Delay or Resume value. / -10, -5 -2 indicates Resume. / 1 to 30 indicates delay. / 0 is off.
8	qkey	integer	The two digit system quick-key for Uniden radios. / A value is required in this field if this is a conventional system type. / NOTE: For Trunked systems, the BCD325P2 & BCD325 use the quick-key from the SITE record rather than the SYSTEM record internally. / However, the quick-key should ALWAYS be included in the system record, as the SDS100 & SDS200 WILL utilize the SYSTEM record rather than the SITE record.
9	hld	integer	The time to hold on this system in seconds (0-255).
10	(varies)	char	Extra definitions for Uniden radios. These are numerical assignments only. Each definition in this field is in the format: XXXn, where 'XXX' is some string, and 'n' is a numerical value (1 or greater). / Additional information on the EXTRA field follows this table.
13	P25wait	integer	Time to wait in ms for a P25 decode. The value must be in increments of 100. Recommended value is 400 for Digital Voice Systems (P25/DMR/Turbo) / NOTE: If P25wait is set to 0 for a digital system, the scanner MAY not stop on transmissions.
14	p25mode	string	P25 'digital squelch' mode. Values are 'Auto', "Manual', 'Default'
15	P25lvl	integer	P25 'Digital Squelch' level. Values are 0-63. For the SDS200, the value must be > 5
16	end_code	string	'Analog','Digital','A+D','Ignore'
17	fleetmap	bitstring	Motorola Fleet Map.
18	custmap	bitstring	Motorola custom map.

Table 4: EXTRA field strings used in System records
string	key	description
SYSTAG	systag	For Uniden radios, this is a number that the user can assign to a channel as an ID. The value in this field is 0-100. If The value is 0, then no tag assignment will be made. Otherwise the value set in the radio will be 1 less then the value specified in this field. / EX: SYSTAG1 - Will assign '0' to the user tag in a Uniden Radio.
EMGALT	emgalt	Emergency Alert Tone. 1-9. If 0, Emergency alert is turned off. / Uniden radios only.
EMGLVL	emglvl	Emergency Alert Volume Level 1-15, If 0, Emergency alert is turned off
EMGPAT	emgpat	Emergency Alert Pattern. 0-ON, 1-Slow flash, 2-Fast flash

### SITE Records
Site records contain information on a specific trunked system location. Site records currently are only used by Unden Dynamic Radios.
Any SITE records that do not reference a valid SYSTEM record, will be marked as orphans. Any TFREQ or BPLAN records that reference orphaned SITE record will also be marked as orphans.
Since site records are used exclusively for Uniden radios, ALL fields used by Uniden radios are defined for the input record.
Site records are NOT processed by the GUI version of RadioCtl.

Table 5: SITE Record Fields
position	key	type	description
1	rectype	string	Record type. (SITE) / Information for Trunking transmission sites.
2	index	integer	Site number index. This number MUST be unique for all SITE records in the file, and must be greater than 0. / If this index is 0, then this record will discarded.
3	Service	string	Description of the Site. Uniden radios limit this to 16 characters. / NOTE: Site Service strings will be displayed on the radio rather than the SYSTEM service string.
4	Valid	binary	If 1, the site will NOT be locked out. / For the SDS radios, the 'valid' field is processed as follows: / When reading a SD Card file: / If 'Avoid' is on, 'Valid' is 0 / else if a quick-key is not defined, 'Valid' is 0 / else if the defined quick-key is turn off, 'Valid' is 0 / else 'Valid' is set 1 / When writing to an SD Card file: / if 'site-qkey' is not a valid number, 'Avoid' will be set REGARDLESS / of the setting of 'Valid' / Else the value of the defined 'site-qkey' will be set by the 'Valid' / setting (1='On', 0='Off')
5	sysno	integer	System index number reference that this SITE is associated with. If this value is 0, or references a non-existent system number, then this record will be treated as an orphan, and any TFREQ or BPLAN records that reference it will also be considered orphaned.
6	qkey	integer	Uniden QuickKey for this site. / For BCD325P2 & BCD396, This quick-key setting will override what is set in the SYSTEM record. / When reading from the BCD325P2: The first non-locked out site with a quick-key defined, will set the SYSTEM quick-key to this value. / When writing to the BCD325P2: If the 'Q' flag is set in the SYSTEM record for this SITE, the quick-key will be turned on in the radio. / For SDS100 & SDS200, this field is not used. A separate field in this record ('site_qkey') is referenced instead. This extra field is needed as quick-keys for SITE records in the SDS radios are considered DEPT quick-keys, rather than SYSTEM quick-keys. / When reading from an SDS radio generated data file, this field will be set to the quickkey for the system it is defined for.
7	hld	integer	Time in seconds to hold on this site when scanning.
8	flags	characters	Flags for the record. Each flag is a single character indicating a special characteristic of this record. Most of the flags affect Uniden Radios, and are not used by the RadioCtl GUI. / Flag characters can be upper or lower case. / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified. / Valid Flag Characters are: / character meaning / A Attenuation is on for this site. / For keyword=value format, ATTEN=1 / O Control Channel Only (BCD325P2 only) / For keyword=value format, , C_CH=1 / Z Enable GPS (BCD325P2 only) / keyword=value format, GPS=1
9	mode	mode	Modulation. Valid values are AUTO, FMn, FMun
10	lat	coord	Latitude of the site. IF DMS format, direction MUST be 'N' or 'S'
11	lon	coord	Longitude of the site. If DMS format, direction MUST be 'E' or 'W'
12	range	number	Number of miles for the range. Decimal number. (SDS200 only)
13	P25wait	integer	Time to wait in ms for a P25 decode. The value must be in increments of 100.
14	p25mode	string	P25 'digital squelch' mode. Values are 'Auto', "Manual', 'Default'
15	P25lvl	integer	P25 'Digital Squelch' level. Values are 0-63. For the SDS200, the value must be > 5
16	p25nac	string	NAC code for P25 systems
17	rf_filter	string	SDS100/SDS200 only. Filter used
18	site_number	string	This is an informational only field. The value is not checked or used by any RadioCtl process. This usually reflects the actual site information for this system.
19	site_qkey	integer	SDS100/SDS200 only. The quickkey for this site. This should be an integer from 0 to 99. If no value set, or the value is NOT a number, the site will be marked 'AVOID' when this record is written to the SD Card. SDS radios CANNOT select a site if a quick-key has not been assigned. / When reading an SDS data file, this will be the quick-key found in the radio's SITE record, and the 'qkey' field in the RadioCtl 'site' record will be set to the 'qkey' value from the system record. / NOTE:This is a 'department' key. When setting this value, the value should be unique with the group quick-keys.
20	(reserved)	-	reserved for future changes

### BPLAN Records
 Uniden radios provide for the ability to specify a custom band-plan for Motorola Systems. The radio will only make use of this record if systemtype is 'motoc'
position	key	type	description
1	rectype	string	Record type. (SITE) / Information for Trunking transmission sites.
2	index	integer	BPLAN number index. This number MUST be unique for all BPLAN records in the file, and must be greater than 0. / NOTE: Normally, There is only one BPLAN per site.
3	siteno	Integer	The site number that this record is for. If this value is 0, or / references a non-existent site, or the site referenced does not reference a valid system number, this record will be orphaned.
4	flags	characters	Any flag characters for this record. / At this time, there are no valid flags defined for BPLAN records.
5	frequency_l1	frequency	Low frequency number 1. Value in Hz
6	frequency_h1	frequency	High frequency number 1. Value in Hz
7	spacing_1	frequency	Spacing number 1. Value in Hz
8	offset_1	integer	Offset number 1. Value is integer from -1023 to 1023
9	frequency_l2	frequency	Low frequency number 2. Value in Hz
10	frequency_h2	frequency	High frequency number 2. Value in Hz
11	spacing_2	frequency	Spacing number 2. Value in Hz
12	offset_2	integer	Offset number 2. Value is integer from -1023 to 1023
13	frequency_l3	frequency	Low frequency number 3. Value in Hz
14	frequency_h3	frequency	High frequency number 3. Value in Hz
16	spacing_3	frequency	Spacing number 3. Value in Hz
17	offset_3	integer	offset number 3. Value is integer from -1023 to 1023
18	frequency_l4	frequency	Low frequency number 4. Value in Hz
19	frequency_h4	frequency	High frequency number 4. Value in Hz
20	spacing_4	frequency	Spacing number 4. Value in Hz
21	offset_4	integer	Offset number 4. Value is integer from -1023 to 1023
22	frequency_l5	frequency	Low frequency number 5. Value in Hz
23	frequency_h5	frequency	High frequency number 5. Value in Hz
24	spacing_5	frequency	Spacing number 5. Value in Hz
25	offset_5	integer	Offset number 5. Value is integer from -1023 to 1023
26	frequency_l6	frequency	Low frequency number 6. Value in Hz
27	frequency_h6	frequency	High frequency number 6. Value in Hz
28	spacing_6	frequency	Spacing number 6. Value in Hz
29	offset_6	integer	Offset number 6. Value is integer from -1023 to 1023

### TFREQ records
 For each site defined, there should be frequencies for that site. These records identify those frequencies used. TFREQ records are ONLY used for trunked systems. Conventional systems use 'FREQ' records.

Table 6: TFREQ record fields
position	key	type	description
1	rectype	string	Record type. (TFREQ) / Frequencies for a given SITE
2	index	integer	Site number index. This number MUST be unique for all SITE records in the file, and must be greater than 0. If index is 0, then the record will be discarded.
3	valid	binary	Usually set as TRUE.
4	siteno	integer	Reference to the site number this frequency is for. If the value is 0, the siteno referenced does not exist, or the siteno referenced does not reference a valid system, this record will be orphaned.
5	frequency	frequency	Frequency in Hz or MHz. If a decimal point is present, the value is assumed to be in MHz. The frequency must not be 0. TFREQ records with a 0 frequency will be marked not valid and ignored.
6	lcn	number	LCN for this frequency. Not all trunked systems use LCN numbers. / If no LCN, the value can be blank, 0 or '-'. Maximum LCN number is 4096
7	mode	modulation	Only 'FMn, or 'FMun' are acceptable for trunked frequencies
8	ccode	string	Color Code (0-15), RAN=0-63 (NXDN), Area=0-1, or 'Srch'. / Default will be 'Srch'
9	flags	character	Flags for the record. Each flag is a single character indicating a special characteristic of this record. Most of the flags affect Uniden Radios, and are not used by the RadioCtl GUI. / Flag characters can be upper or lower case. / For keyword=value format, the flag field is NOT used. Instead the individual key is specified. / At present, no flags are defined for this record type.

### GROUP Records
  GROUP records identify frequencies that have some common grouping. For example, a group might be created called FIRE which identifies all frequencies associated with Fire Departments. The RadioCtl GUI allows for scanning by these GROUP records.
Uniden Dynamic Radios also allow for processing and storing group information. These radios can save up to 20 groups assigned to a system. In order for any GROUP record to be stored in a Uniden radio, it MUST be associated with a SYSTEM record. The RadioCtl GUI has no restrictions on the number of GROUP records, or requirement of SYSTEM linkage.
The some ICOM radios also utilize group records. However, at the current time, there is no way to directly read or write these values. If ICOM updates the firmware in these radios, this situation may change. Group information in ICOM radios CAN be written to an SD card for setting into the radio.
All other radios do not have the ability to store GROUP information.

 Table 7: GROUP Record Fields
position	key	type	description
1	rectype	string	Record type. (GROUP). / Categories of the various services that the radio may receive.
2	index	integer	Group number index. This number MUST be unique for all Group records in the file, and must be greater than 0. If this value is 0, the record will be discard.
3	service	string	Description of the group. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio.
4	valid	binary	If TRUE, the Group will be used by the program and by the radio (if the radio supports it). If FALSE, the group will be locked-out in the radio (and in the GUI). / Note: When storing into Uniden BCD radios, the VALID flag will determine if the GROUP quickkey is set on or not. For these radios, a defined group is never locked-out.
5	sysno	integer	System index number that this GROUP is part of. / If this value is 0, or references a non-existent system number, then this record will be marked as an orphan.
6	flags	character	Flags for the record. Each flag is a single character indicating a special characteristic of this record. Most of the flags affect Uniden Radios, and are not used by the RadioCtl GUI. / For keyword=value format, the flag field is NOT used. Instead the individual key is specified. / Currently there are no valid flags defined for this record type.
7	(none)	(none)	Reserved field for future enhancments
8	(varies)	string	Extra definitions for various radios. These are numerical assignments only. Each definition in this field is in the format: XXXn, where 'XXX' is some string, and 'n' is a numerical value (1 or greater). / Additional information on the EXTRA field follows this table.
9	gqkey	integer	Uniden Group quickey (0-9). Although not required by the Radios, A quick-key should ALWAYS be defined for Uniden radios, or the group can never be de-selected.
10	rf_filter	string	'Global','Invert','Auto','Normal','Wide Normal', 'Wide Invert', "Wide Auto', 'Off'. Only used by the Uniden SDS100/SDS200
11	lat	coord	Latitude of the group. If DMS format, direction MUST be 'N' or 'S'
12	lon	number	Longitude of the group. If DMS format, direction MUST be 'E' or "W'
13	range	number	Number of miles for the range. Decimal number. (SDS100/SDS200 only)

 The EXTRA field allows for definitions in positional records without affecting the location of other fields. This field consists of one or more strings in the form: XXXn, where 'XXX' is some keyword, and 'n' is a number > 0. Keywords are NOT case sensitive. Multiple strings can be specified in this field. However, each string MUST be separated by a blank. If a string represnting that keyword is NOT present, the value will be set to the default when reading the file. If the value is set to 0 when a file is written by the program, the string in the EXTRA field will NOT be written. Extra fields are NOT specified on records using the KEYWORD=VALUE format.
Table 8: EXTRA field strings used in GROUP records
string	key	description
SCANGRP	scangrp	Scan group for ICOM radios. Value can be 0-9. / For the IC-705 The value must be 0-3. For The IC-8600, the value must be 0-9. / This value will be used if the scangrp value in the FREQ records is 0. / A value of 0 indicates that frequencies associated with this group will NOT be included in any scan group unless specified on the FREQ record.
SVCODE	svcode	Service code (1-37,208-216). Only used by the Uniden SDS100/SDS200

### FREQ records
 FREQ records define individual frequencies or trunk ids (TGID). The records include Modulation, service and other information that MAY be stored in a radio's memory channel. These records are also used by the RadioCtl GUI program.
If the record defines a Trunked Group ID (TGID), the frequency value should be 0. A 0 frequency for a record that does NOT contain a valid TGID is assumed to be a blank channel. TGIDs are only stored to and fetched from Uniden Radios.

Table 9: FREQ Record Fields
position	key	type	description
1	rectype	string	Record type. (FREQ). / Frequency and other information used by both The RadioCtl program and stored in the radio's memory.
2	index	integer	Freq number index. This number MUST be unique for all FREQ records in the file, and must be greater than 0. / If this value is 0, this record is discarded.
3	service	string	Description of the Frequency. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio.
4	valid	binary	If TRUE, the Frequency will be marked for scanning and selection by the RadioCtl GUI and by the radio.
5	groupno	integer	GROUP index number that this FREQ record is part of. / If this number is 0, or references a non-existent group index, or the referenced group does not reference a valid SYSTEM record, then this record will be orphaned.
6	flags	character	Single character flags indicating some attribute of this record. Characters are NOT case sensitive. Multiple flags can be specified. / Note that some radios have the ability to store attenuation in the radio's memory channels. For these radios, there is a separate attenuation flag. / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified. (ex: ATTEN=1) / Valid flag characters are: / char key meaning / A atten Attenuation is on for this frequency for ALL radios. / 2 sdaatt Attenuation is on if this is a Uniden SDS100 or SDS200 model radio. / 3 bcdatt Attenuation is on if this is a Uniden BCD325P2 or BCD396 model radio. / 4 r30att Attenuation is on if this is a ICOM IC-R30 model radio. / G tgid This is a TGID (Trunked Group ID). Only affects Trunked systems. / For keyword=value format, this flag is assumed if the value of TGID is set. / Not used in the RadioCtl GUI. / P priority Priority is on / + oplus Positive offset. ICOM/Kenwood Radios only / - ominus Negative offset, ICOM/Kenwood Radios only
7	channel	integer	Channel number for the radio. Valid values are 0 thru 9999, -1, ‘-’ , ‘.’ or blank. / If the value is not a number between 0 and 9999, the record MAY be ignored for certain operations. / If the value is outside of the radio’s range, the record will also be ignored. / NOTE:For certain ICOM radios, the channel number represents two parts: The Group and the Channel in that group. For these radios, the last two digits are the Group and the first two are the channel in that group. / EX: Channel 1234 would be ICOM group 12, channel 34.
8	frequency	frequency	Frequency in Hz or Mhz. If a decimal point is present, the value is assumed to be in MHz. The frequency should NOT be 0 unless this is a TGID record, or the radio's channel is to be cleared.
9	mode	mode	Modulation string. Acceptable values are AM, FM, FMw, FMn, FMun,LSB, USB, AUTO and possibly others (depending on the radio). Case of the string is not important. If AUTO is specified, RadioCtl (or the radio) will attempt to adjust the modulation based on the Frequency. Note that some radios do not allow all modulations, or cannot change the modulation. This field is ignored if this is a TGID record.
10	tgid	tgid	Trunked Group ID. If the 'G' freq_flag is set, this field will be used for Uniden Radios only. A TGID record ignores the FREQUENCY and MODE fields.
11	tone	decimal or hex	A decimal number indicating the sub-audio tone, or digital ID used for squelch or repeater operation. Tones can be CTCSS (67.0 to 254.1) or DCS (023 to 754), as well as P25 NAC (0-FFFx), DMR Color Code (0-15), and NDXN RAN (0-63) values. The value can also be 'off' or 0 indicating no tone used. / If the specified tone does NOT exactly matched the predefined values, the program will attempt to match to the correct value. / What the tone represents is determined by the TONE_TYPE field. / NOTE: Not all radios have the ability to utilize sub-audio tones or IDs.
12	tone_type	string	Type of tone that the 'tone' field represents. This field is NOT case sensitive. The tone type MUST be compatible with the audio type specified in the 'adtype' field. / In order for tone processing to be valid, the 'mode' MUST be ''FM', 'FMn', or 'FMun'. / Valid values are: / value meaning / Off Tone is off, Tone field is ignored / CTCSS The Tone field is a CTCSS frequency. Tone is used to squelch unless the CTCSS tone value is being transmitted. / DCS The Tone field is a DCS code. Tone is used to squelch unless the code is transmitted. / If the DCS code is > 999, then the 'Reverse' indicator in the radio will be set. / This ONLY applies to the ICOM IC-R30. This indicator is ignored for all other radios. / RPTR The tone field is a Repeater keying tone. The radio will add the tone to any transmissions. (IC-703 & Kenwood only) / NAC The tone is a DCR NAC value.Thee squelch will not break until the P25 NAC is recognized. / The 'tone' field is assumed to be in HEX. / CCODE The Tone field is a DMR Color Code. The squelch will not break until the DMR Color code is recognized. / RAN The Tone field is a NXDN RAN value. / The 'adtype' field MUST be 'NXDN' or 'NXDNVN'
13	dlyrsm	integer	Delay or Resume value. / -10, -5 -2 indicates Resume. / 1 to 30 indicates delay. / 0 is off.
14	(varies)	string	Extra definitions for various radios. These are numerical assignments only. Each definition in this field is in the format: XXXn, where 'XXX' is some string, and 'n' is a numerical value (1 or greater). / Additional information on the EXTRA field follows this table.
15	adtype	string	Audio type. This field affects how an audio signal is processed by the radio. It also affects what 'tone_type' can be used for squelch processing. / Valid values are: / value usage / ALL Type of audio will be determined by the radio, and the 'tone_type' field. / This is valid for ALL radios. / ANALOG Only Analog voice/tone processing is done. / This is valid for ALL radios. / DIGITAL Only digital voice/tone processing is done. . / NXDN The audio is an NXDN-N (12kHz) digital signal. / NXDNVN The audio is an NXDN-VN (6kHz) digital signal. / P25 The audio is a P25 digital signal. / DMR The audio is a DMR digital signal / DSTAR The audio is a D-Star Digital signal.
16	lat	coord	Latitude of the transmitter for this frequency. Can be entered in decimal or DMS (dd:mm:ss.ss:direction). Only used when creating records for the ICOM IC-R30 SD card. If '0' or '', this field is not set.
17	lon	coord	Longitude of the transmitter for this frequency. Can be entered in decimal or DMS (dd:mm:ss.ss:direction). Only used when creating records for the ICOM IC-R30 SD card. If '0' or '', this field is not set.
18	(reserved)	-	Reserved for future changes
19	sfrequency	frequency	Split or offset frequency in Hz or Mhz. If 0, or the frequency is the same as the main frequency, (Field 8). no split frequency is indicated. / If the oplus (+) or ominus (-) flags are indicated, this will be treated as an offset frequency. / Split frequency or offset usage is ONLY appropriate for models that can transmit (ICOM IC-705, ICOM IC-703 and Kenwood TH-F6A). / However, The ICOM IC-R30 will recognize offset usage ONLY when writing to the SD-Card.
20	smode	mode	Split modulation. If specified, identifies a modulation for a split channel to be stored to or retrieved from the radio. If SFREQUENCY given, but SMODE is not, the modulation specified in the MODE field will be used. SFREQUENCY must be specified for SMODE to be processed.
21	stone	decimal	Split tone. If specified, and is not 0, it identifies a tone (CTCSS/DCS/REPEATER) for a split channel to be stored to or retrieved from the radio. If SFREQUENCY given, but STONE is not, the tone specified in the TONE field will be used. SFREQUENCY must be specified for STONE to be processed.
22	stone_type	string	Split tone type. If specified, and is not 'off', this will identify a tone type (CTCSS/DCS/REPEATER) for a split channel to be stored to or retrieved from the radio. If SFREQUENCY given, but STONE_TYPE is not, the tone specified in the TONE_TYPE field will be used. SFREQUENCY must be specified for STONE_TYPE to be processed.

Split frequencies or offsets are used by radios that allow for transmission (on Ham Bands), as well as reception by the ICOM R30. These splits are defined using ONE of these methods:
- '+' or '-' for the flag value and a frequency offset for the sfrequency value. The offset MUST be greater than 100 kHz and less than 100 MHz.
  EX: ominus=TRUE,sfrequency=.6, frequency=146.61
- No '+' or '-' specified for the flag, and an sfrequency value different than the frequency value. The difference between the frequency and the sfrequency must be greater than 100 kHz and less than 100 Mhz.
  Examples: frequency=442.0, sfrequency=447.0
  frequency=442.0,oplus=TRUE

Note that the ICOM R30 only supports offset specification. If the second format is specified when creating the SD Card output for tthis radio, the offset value will be calculated.

The Kenwood TH-F6A only uses split frequencies. If the offset format is specified for this radio, RadioCtl will calculate out what the split frequency should be when storing the record into the Radio's memory.

Audio type and tone type specifications require a number of rules to be followed.
- Only one tone type per FREQ is allowed
- The Tone-Type must be consistant with the Audio-Type
- Digital audio/tone types are only valid for certain radios.
- Digital audio/tone types are NOT supported on the GUI panels.

Table 10: Audio/Tone consistancy chart
audio-type	allowed tone-type	Radios supported
ALL	Any	All
DIGITAL	RAN,NAC,CCODE	ICOM-R30 / UNIDEN BCD325P2 / UNIDEN SDS100 / UNDEN SDS200
ANALOG	CTCSS, DCS, RPTR	All except ICOM R7000.. / RPTR is only for ICOM IC-705/Kenwood TH-F6A
NXDN, NXDNVN	RAN	ICOM-R30 / UNIDEN SDS100 / UNDEN SDS200
P25	NAC	ICOM-R30 / UNIDEN SDS100 / UNIDEN SDS200 / UNIDEN BCD325P2
DMR	CCODE	UNIDEN SDS100 / UNIDEN SDS200 / UNIDEN BCD325P2
DSTAR	DSQL	ICOM-R30

The EXTRA field allows for definitions in positional records without affecting the location of other fields. This field consists of one or more strings in the form: XXXn, where 'XXX' is some identifier, and 'n' is a number > 0. Identifiers are NOT case sensitive. Multiple strings can be specified in this field. However, each string MUST be separated by a blank. If a string represnting that keyword is NOT present, the value will be set to the default when reading the file. If the value is set to 0 when a file is written by the program, the string in the EXTRA field will NOT be written. Extra fields are NOT specified on records using the KEYWORD=VALUE format. Instead, the key iteslf is specified.

     Examples: ADTYPE1 ### Extra field positional format
        adtype=1 ### keyword=value format

Table 11: EXTRA field strings used in FREQ records
string	key	description
ADTYPE	adtype	Audio type for Uniden Radios. A 1 indicates that this will be an analog only channel. A 2 indicates Digital only. A 0 (or not specified) indicates both. / NOTE:If CTCSS or DCS tone squelch is used, this value MUST be 1. / If Digital squelch modes are used, then the value MUST be 2. / If these settings are not followed, then the radio may not respond correctly for tone squelch.
BCDTAG	bcdtag	For Uniden radios, this is a number that the user can assign to a channel as an ID. The value in this field is 0-1000. If The value is 0, then no tag assignment will be made. Otherwise the value set in the radio will be 1 less then the value specified in this field. / EX: BCDTAG1 - Will assign '0' to the user tag in a Uniden Radio.
EMGALT	emgalt	Emergency Alert Tone. 1-9. If 0, Emergency alert is turned off. / Uniden radios only.
EMGLVL	emglvl	Emergency Alert Volume Level 1-15, If 0, Emergency alert is turned off
EMGPAT	emgpat	Emergency Alert Pattern. 0-ON, 1-Slow flash, 2-Fast flash
RFGAIN	rfgain	For the ICOM R30 only, this is the value of the RFGAIN setting. This value must be between 0 and 9. If value is 0, or not set, RFGAIN will be set to RFMAX.
SCANGRP	scangrp	Scan group for ICOM radios. Value can be 0-9. / This is an indicator that the channel is to be included in a Select Memory Scan. / For the IC-705 The value must be 0-3. For The IC-8600, the value must be 0-9. / A value of 0 indicates that the channel will NOT be included in any scan group. / This value overrides any value set in the associated GROUP record.
SVCODE	svccode	Service code (1-37,208-216). Only used by the Uniden SDS100/SDS200 / Note that the SDS radios MUST have a service code set in the channel, or the channel will NOT be included in scanning,
VOLOFF	voloff	Volume offset for Uniden Radios. This value is 0-6. Values 4,5, & 6 represent offsets of -1, -2 & -3.

### SEARCH records
 These records are used by the RadioCtl GUI. In addition, some radios (most notably the Uniden) allow for search records to be stored and recalled. For the Uniden, only the first 10 records can be saved in the radio.

Table 12: SEARCH record fields
position	key	type	description
1	rectype	string	Record type. (SEARCH). / Search information used by both The RadioCtl program and possibly stored in the radio's memory.
2	index	integer	Search number index. This number MUST be unique for all Search records in the file, and must be greater than 0.
3	service	string	Description of the Search. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio.
4	Valid	binary	If TRUE, the Search will be used by the program and by the radio.
5	lowfreq	frequency	Starting frequency for the search. Frequency can be in Hz or Mhz. If the number contains a decimal point, Mhz is assumed.
6	highfreq	frequency	Ending frequency for the search. Frequency can be in Hz or Mhz. If the number contains a decimal point, Mhz is assumed.
7	Step	integer	Frequency step for the search. Step value is in Hz. / NOTE: Step CANNOT be 0!
8	mode	mode	Acceptable values are AM', FM, FMW, FMN, LSB, USB, AUTO and possibly others (depending on the radio). Case of the string is not important. If AUTO is specified, RadioCtl (or the radio) will attempt to adjust the modulation based on the Frequency. Note that some radios do not allow all modulations, or cannot change the modulation.
9	flags	character	Flags for the record. Each flag is a single character indicating a special characteristic of this record. / Currently no flags are defined for the SEARCH record.
10	dlyrsm	integer	Delay or Resume value. / -10, -5 -2 indicates Resume. / 1 to 30 indicates delay. / 0 is off.
11	hld	integer	Hold in seconds.
12	(varies)	string	Extra definitions for various radios. These are numerical assignments only. Each definition in this field is in the format: XXXn, where 'XXX' is some string, and 'n' is a numerical value (1 or greater).
13	p25wait	integer	P25 wait time in ms (in increments of 100). / Only used with Uniden radios.
14	agc_analog	binary	If TRUE, AGC used for Analog. / Only used with Uniden Radios.
15	agc_digital	binary	If TRUE, AGC used for Digital. / Onlu used with Uniden Radios.

### POWERMSG record
  This is a single record that defines the power on message for the radio. Only a small number of radios (Uniden and Kenwood) allow for setting a power on message.
Only one POWERMSG record is used. If multiple are found in a file (or group of files) the last one read will be the one used.
The POWERMSG record is typically specified using KEY=VALUE format. However, positional format is also acceptable.
Table 13: POWERMSG Record Fields
position	key	type	description
1	rectype	string	Record type. (POWERMSG).
2	msg1	string	First line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.
3	msg2	string	Second line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.
4	msg3	string	Third line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.
5	msg3	string	Fourth line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.

### LIGHT records
This is a single record that defines the behavior of the back-light for the radio. Only a small number of radios (Uniden and Kenwood) allow for setting back-light behavior
Only one LIGHT record is used. If multiple are found in a file (or group of files) the last one read will be the one used.
The LIGHT record is typically specified using KEY=VALUE format. However, positional format is also acceptable.

Table 14: LIGHT Record format
position	key	type	description
1	rectype	string	Record type. (LIGHT).
2	event	string	When to turn on the light. Values are: / value description / ON Light is always on / OFF Light is always off / KEY / KY Light goes on briefly when a key is pressed (Uniden Only) / SQ Light goes on when there is a signal (Uniden Only) / 10 Light goes on for 10 seconds when the LIGHT key is pressed (Uniden only) / 30 Light goes on for 30 seconds when the LIGHT key is pressed (Uniden only)
3	bright	number	Brightness (1,2 or 3). Uniden only

### BEEP records
This is a single record that defines the volume of the key-press 'Beep'. Not all radios have the ability to set this value. For some radios (such as the Kenwood), the key-press sound is only on or off.
Only one BEEP record is used. If multiple are found in a file (or group of files) the last one read will be the one used.
The BEEP record is typically specified using KEY=VALUE format. However, positional format is also acceptable.

Table 15: BEEP Record format
position	key	type	description
1	rectype	string	Record type. (BEEP).
2	volume	number	Volume of the 'Beep'. Value is 0 (off), 1-15 (15 is the loudest). / If a value of 16 (or greater) is given for the BCD325P2, then 'Auto' will be set in the radio. For all other radios, anything > 15 will be considered maximum. / For radios without the ability of variable volume level, any value greater than 0 will turn ON the Beep.

### LOCKFREQ records
  These records are strictly for Uniden radios. They indicate a frequency that is locked out from scan or search. These records are NOT used by the RadioCtl GUI program.
Table 16: LOCKFREQ record fields
position	key	type	description
1	rectype	string	Record type. (LOCKFREQ).
2	frequency	frequency	The frequency (Hz or Mhz) that is locked out

### IFXCHNG records
   These records are strictly for Uniden radios. They indicate a frequency that will have a different IF (Intermediate frequency) to eliminate 'birdies'. These records are NOT used by the RadioCtl GUI program.
Table 17: IFXCHNG record fields
position	key	type	description
1	rectype	string	Record type. (IFXCHNG).
2	frequency	frequency	The frequency (Hz or Mhz) that is exchanged

### SYSKEY records
  These records are strictly for Uniden radios. They identify the keys (00-99) for each system defined in the radio. These records are NOT used by the RadioCtl GUI program.
Table 18: SYSKEY record fields
position	key	type	description
1	rectype	string	Record type. (SYSKEY). / System Key assignments. This record is ONLY utilized by Uniden Dynamic radios. It is also not processed by the GUI program.
2	sys=value	binary | -	'sys' is 0-99, value is 0 (Off),1 (On) or '-' (not set)

### LOOKUP records
  LOOKUP records are used to identify known frequencies. These records are used only by the RadioCtl GUI program. They are not stored in any radio.
Table 19: LOOKUP record fields
position	key	type	description
1	rectype	string	Record type. (LOOKUP).
2	frequency	frequency	The frequency (Hz or Mhz) for this assignment. Every frequency in this file should be unique. If there are multiple entries with the same frequency, the program will only make use of the first one found in the file.
3	service	string	Description of the usage of this Frequency. Any valid text can be used. There is no limit on the length of this value. However, if the string gets assigned to a variable that may be stored in a radio, that radio MAY limit the length.

### FLIST Records
 These are used for building the flist.cfg file in the SDS200 SD card. This file defines all of the Favorites lists for the radio. Each record will translate to a record in this configuration. The records are ONLY processed by the csv2sds command of RadioWrite.pl. These records can be included in any RadioCtl CSV file, and will be ignored by all other processes.

Table 20: FLIST record fields
position	key	type	description
1	rectype	string	Record type. (FLIST) / Favorites List entry
2	filename	String	Filename. Must be in the form 'f_xxxxxx.hpd' where 'xxxxxx' is 000000 to 999999. This format is required by the Radio (not RadioCtl).
3	service	string	The name of the favorite. Any number of characters can be entered, but the radio will limit it to 64 characters
4	monitor	Binary	Monitor the favorite. On=Monitor this favorite. Off=Don't Monitor This Favorite
5	useloc	Binary	Use Location. On=Use location based scanning. Off=Don't use location based scanning. / NOTE: Unless GPS coordinates are carefully entered in ALL lists, it is recommended that this ALWAYS be off.
6	qkey	number	Quick-key for this favorites list. 00-99.
7	systag	number / 'Off'	User setable tag number. The value in this field is 0-100. If The value is 0, then no tag assignment will be made. Otherwise the value set in the radio will be 1 less then the value specified in this field. / EX: SYSTAG1 - Will assign '0' to the user tag for that system.
8	keys_on	number	A list of System Quick-keys that should be turned on for this Favorites. Each key number to turn on MUST be separated by a blank.

### TONEOUT Records
   TONEOUT records are used exclusively for Uniden Radios. They define Tone-Outs that are stored in the radio for use with local fire and ambulance services. TONEOUT records can be stored in BCD radio memories (BCD396T/BCD325P2) using the TONEOUT command of RadioWrite. They can also be saved to the SD-Card for the SDS100/SDS200.

Although this table indicates the position of each field in a record, TONEOUT records are usually kept in KEYWORD=VALUE format.

position	key	type	description
1	rectype	string	Record type. (TONEOUT) / Tone-out setting
2	index	integer	number index. This number MUST be unique for all TONEOUT records in the file, and must be greater than 0.
3	service	string	The name of the Tone-Out. Any number of characters can be entered, but the radio will limit it to 16 characters
4	channel	integer	Tone-Out channel. For the BCD radios, this must be a number between 0 and 9 (representing Tone-Out settings 1-10). / For SDS radios, the number can be beween 0 and 99.
5	frequency	frequency	The frequency (Hz or MHz) used by this agency. If a decimal point is included in the value, it is assumed to be in MHz.
6	mode	mode	Modulation string. Acceptable values are FM, FMn, or AUTO. / Any other modulation will be rejected by the radio.
7	toneout_a	frequency	The first tone value. This is specified in Hz. / The value must be 0, 250.0 to 3500.0.
8	toneout_b	frequency	The second tone value. This is specified in Hz. / The value must be 0, 250.0 to 3500.0.
9	flags	character	Single character flags indicating some attribute of this record. Characters are NOT case sensitive. Multiple flags can be specified. / For KEY=VALUE format, the flag field is NOT used. Instead the individual key is specified. (ex: ATTEN=1) / Valid flag characters are: / char key meaning / A atten Attenuation is on for this Tone-Out / J agc_analog AGC Analog is on. (Not used on BCD396T)
10	dlyrsm	integer	Specific values are 0 (no delay), 1,2,3,4,5,10,30. Any values greater than 30 will set the delay to 'Infinite'.
11	emgalt	integer	Alert Tone. 1-9. If 0, Emergency alert is turned off.
12	emglvl	integer	Alert Volume Level 1-15, If 0, Emergency alert is turned off
13	emgpat	integer	Alert Pattern. 0-On, 1-Slow, 2-Fast (not used on BCD396T)
14	emgcol	integer	Alert Color, 0 - Off, 1-Red. (not used on BCD396T) / NOTE:The SDS radios allow for colors other than RED. Numbers between 2 & 9 will translate to these colors when used by the SDS Radios. For the BCD325P2, numbers > 1 will translate to 1.

# Log File
The RadioCtl GUI can save activity information when scanning or searching. This includes frequency, signal strength, duration of signal, and a time stamp. The information is saved in a separate, comma delimited ('CSV') file. The directory where this file is placed is defined in the configuration file. The name of the file is set in the Operation Options panel on the Main window. If the 'Log Events' on this panel is checked, information is saved in this file. Records will be logged ONLY during scan or search operations, unless
the 'Update database in Manual' option is also selected.

Any filename can be specified. If the file specified does NOT exist, it will be created when the first log record is saved. If it DOES exist, each log record will be appended to the existing file. When a file is first created, the first record will indicate the field names.

Each record in the log file is a number of fields, each separated by a comma (','). This file can be viewed using any text editor, or imported into a spreadsheet program.

Table 21: Log File Records
position	description
1	Time Stamp. Human readable data/time for the log entry
2	Received Frequency in MHz
3	Modulation of the signal
4	Duration in seconds that a signal was detected
5	RadioCtl signal level (0-9)
6	RSSI (Received Signal Strength Indicator) if available. Not all radios return a RSSI indicator.
7	Channel number (if available). For dynamic radios, this may be blank
8	Service (if available)

# Configuration File
The configuration file is always named radioctl.conf. This file is used to configure the various radios that are used in the program, as well as some defaults. The file MUST reside in the home directory of the user. All radios that are to be utilized by RadioCtl must be defined in this file.
The format of each record of the file is:
   record_type,keyword=value,keyword=value, ....
There should be NO space between the keyword, '=' and value. As with data files, any record that starts with '*' or '#' is ignored. The record-type is NOT case sensitive, nor are the 'keyword's. Each keyword/value can be specified in any order. Any value missing will be set to the default UNLESS the keyword is required. If a required keyword is missing on a record, the program will terminate with an error message.
Important: Because of the way that configuration records are processed, no value can contain a comma (',') an equal sign ('=') or a '#';

### RADIO record type
This record type starts the definition for a radio. Any radio that is to be used by RadioCtl (GUI or Command line) MUST be defined with a RADIO record.

The following keywords are recognized:

keyword	Description
Name	Name of the radio. Any combination of alpha-numeric characters is allowed for the name EXCEPT ',' (comma) '=' (equal sign) or '#'. / The name MUST be unique. The name is NOT case sensitive so 'Bearcat' and 'BEARCAT' will be the same radio. / This is a required key. If this key is missing, then the program will terminate.
Protocol	The protocol for the radio. Must be one of the following: / procotol Radio models / Local Simulated radio. By default, one simulated radio is defined in the GUI. / Bearcat BC895XLT / Kenwood TH-F6A / Uniden BCD325P2, BCD396xlt, SDS100, SDS200 / Icom R-7000,IC-703,IC-R30 / AOR8000 AOR8000 / The protocol value is NOT case sensitive. Note that the models above are the ones that have been tested. Other models of the make of the radio MAY also work. / Protocol is a required key. If this key is missing, then the program will terminate.
Model	Model name. This value MUST be specified.
radioaddr	For ICOM radios only, this is a 1 byte hex value that the radio uses to identify commands that are for that radio. If not specified, the program will attempt to set this address based on the Model specified. If this address and the model are missing from this record, then the default address will be set to '08'x (R-7000 default address).
sdir	For radios with SD cards (ICOM R30, Uniden SDS200), this will be a directory for storing files that are destined for that Radio's SD card. This directory is used with the CSV2SDS and CSV2R30 commands. If not specified, the output will be stored in the default output directory, or the directory specified for those commands.

### DIRECTORY Record Type
This record defines the defaults for various directories used in the program. If a value is not defined in the configuration file, the default directory will be ~/radioctl

Table 22: DIRECTORY record type keys
keyword	Description
recdir	Directory to hold any recordings (.wav files).
tempdir	Default directory for most output files.
logdir	Directory to hold any log files.

### LOCATION Record Type
This record type defines a particular location that may be used in the program. A default location 'Home' is defined by RadioCtl. This can be overriden by specifying a 'Home' location in the confuguration files. For some operations involving GPS coordinates, the coordinates can be specified using the name of the coordinates as defined in the configuration file.
NOTE:All keywords listed MUST be present (and valid) or the LOCATION record will be discarded.

keyword	Description
name	Name of this location. The case of the name is not significant. Ex: mine or Mine will be the same location. / If the name is 'Home', this will be used as the default location wherever coordinates are needed, but are not specified.
lat	Latitude of this location. Value can be Decimal (ex:46.1234) or DMS (ex:80:14:33.1:N). / Case of the direction in DMS is not significate ('n' is the same as 'N'). For DMS direction MUST be 'N' or 'S'. A negitive decimal indicates 'S'.
lon	Longitude of this location. Value can be Decimal (ex:-75.1234) or DMS (ex:73:14:33.1:W). / Case of the direction in DMS is not significate ('w' is the same as 'W'). For DMS direction MUST be 'E' or 'W'. A negitive decimal indicates 'W'.

# GUI configuration File
  This file is created and updated exclusively by the GUI program. It is used to save and restore various parameters, panel settings, and screen positions during the course of the GUI operations. The file is stored in the User's HOME directory ('~') with the name radioctl.vars.

Each record identifies a variable in RadioCtl and what the value should be when the program is started. The variables are usually multi-keyed hashes. In general the record will be interpreted as a PERL assignment statement.

The user should NOT modify the contents of this file, as it could cause the RadioCtl program to fail. However, the file CAN be erased before starting RadioCtl if the user desires all settings for the program to revert to the original values.