        RADIO CONTROL DATA FILE FORMATS

Last update:09/14/23

# INTRODUCTION

RadioCtl for Linux utilizes a number of different input and output files. This document describes the formats of these files. Definitions of the various terms used, and the operation of the RadioCtl program are described in the RadioCtl-Operation manual.

# File Formats
There are three different file types in use in the program. The first is the data files. These contain frequencies, groups, systems and other settings for the radios. These files can be in several formats, and can reside anywhere on the user's computer system.

The second file type is the configuration file for the radios being used. This file defines the name, protocols and other important information about each radio available to RadioCtl It also provides some customization for some program defaults. There should only be one of these files residing in the user's HOME directory.

The third file type is used by the GUI program for saving and restoring various program settings. There is only one of these, and the user normally does not need to make changes to this file.

## Record formats
  In general ALL RadioCtl file records are in the format:

     record_type,field_data,field_data,….

where ‘record_type’ identifies the contents of the data fields that follow.
Each field is separated by a comma. The record is terminated by a Line-Feed (ASCII Code 10) Character. This is the normal Linux character when editing the file. The record can also be terminated by an additional Carriage-Return (ASCII Code 13) which may be added by Windows Text Editors.

The record can be positional, where the field is determined by the position in the record.
Or the record can be non-positional, where each field is determined by a keyword=value statement.
If the first field after the record_type contains a ‘=’, the rest of the record is assumed to be in non-positional format. Otherwise positional format is assumed. Keywords and record_type are NOT case sensitive.
For non-positional, each field can be specified in any order. Values not specified and not required will be set to a default value.

examples:

#non-positional format
FREQ,SERVICE=Fire Dept,index=1,Frequency=150.230,Mode=FMn,Valid=1,groupno=2,Channel=5

#Same record in positional format
freq,1,Fire Dept,1,2,5,150.320,FMn

Important: Because of the way that data records are processed, no value for either record format can contain a comma (',') an equal sign ('=') or a hash-tag ('#'), as this characters have special meaning.

In general, either format is acceptable for most record types. The positional format is easier to read, but harder to create. The key=value format is easier to create, but not as easy to locate specific values. The default output for most records is positional. However, trunked systems default to non-positional.
NOTE: There ARE a few record types that ONLY understand the key=value format.

If a record starts with a ‘*’ or a ‘#’ it is a comment record. In general, comment records can be placed anywhere in the file. There is some additional processing that MAY happen with comment records. See the section Comment records for details.

In addition, a ‘#’ can be placed at the end of a data record to include comments that are NOT part of the record. Any values for that record that are not set when ‘#’ is encountered will be set to default values.

## Record Field Types
Fields specified for each record must conform to the type defined for that field. For example a Number field CANNOT contain letters. When the program reads a data file, it will ignore any record that contains the wrong type in a field.
Table 1: Field Types
type	description
Integer	Whole, positive or negative number including 0. / For fields that a 0 value is significant, a -1 is usually set to indicate the value is not to be set.
Decimal	Positive Number with (or without) a decimal point, or 0
Hex	A hexadecimal integer. Value contains only digits 0-9 and a,b,c,d,e,f. The case of the letters is not important (F2 is the same as f2.)
String	Any combination of letters, numbers and punctuation. / 'cntrl' characters (other than carriage-return and line-feed) should be avoided, as they can interfere with the processing. / NOTE: Due to the way that the data files are parsed, a comma (',') or equal sign ('=') cannot be included in any string.
Binary	TRUE or FALSE. 1, T, True, Y, Yes, On, (not case sensitive) are all interpreted as TRUE. All other entries are interpreted as FALSE.
Flag	A single character indicating a binary setting for a record. If the flag character is present in the field, then that value is considered to be a 1 (On). If the flag character is not present in the field, then the value is considered to be 0 (Off). / For Flag fields, multiple chars can be specified. Flag characters are NOT case sensitive. / NOTE:Flag characters are used ONLY in positional record formats. / For non-positional records, the keyword associated with that flag is used.
Extra	Extra field values for positional records. Each record type usually has an ‘Extra’ field to be used for positional formats. This allows additional settings WITHOUT modifying the positions of other fields. / Extra field values are in the format / key=value key=value … / Where ‘key’ is the keyword for the record, and value is usually a number. / No blanks are allowed between ‘key’, ‘=’ or the value. Multiple specifications in a single extra field have blanks between each specification. / For non-positional records, the keys that would be specified in an Extra field are specified just like any other field.
Index	A positive integer that is assigned to a specific record. Most record types in a RadioCtl data file MUST have an index that is unique for that record type. Duplicated or missing indexes can cause the program to generate a number of errors. / A number of record types reference other record types using this index. No Index value can be less than 1.
Frequency	A positive integer or decimal number. If Decimal point is included in the value, then the value is assumed to be in MHz. Otherwise the value is assumed to be in Hz. A frequency of 0 indicates an empty channel or ignored setting. Frequency may also be 0 if the record represents a Trunked Group ID (TGID)
Mode	Modulation string. Valid values are AM, FM, FMn, FMw, FMn, CW, SSB, LSB, USB, AUTO. Additionally digital decode modulations can be specified. Those are D-Star, dPMR, NXDN-VN, NXDN-N, DCR, DMR and P25. The string is NOT case sensitive. Not all modulations are valid for all radios. The program may modify the modulation based on the current radio. If AUTO specified, the modulation will be set based on the frequency. Currently, only certain ICOM radios recognize the digital modulations. For all other radios, these will be translated to FMn.
TGID	Trunked Group ID. Can be in format nn-xxx or nnnn (where 'n' & 'x' are numbers).
Coord	GPS coordinate. Can be a Decimal number, or DMS format (DD:MM:SS:direction) / For Decimal number, the sign indicates N,S,E or W. For DMS, the direction is NOT case sensitive.
protocol	The name of a RadioCtl supported protocol. Currently the following protocol names are recognized: Uniden, ICOM, Kenwood, AOR8000, Bearcat
Bitstring	A series of 1s and 0s only. Ex: 10010101

# Data Files
  These files contain frequencies, modulations and other parameters that may be sent to or read from the various supported radios. These files can be created and modified by the user, or they can be created by the RadioCtl program. Data files are loaded into the GUI using the Files menu item. Data files can also be read, updated, or created using the command line program (radiowrite). All data files are standard ASCII, with each record terminated with a LF character (ASCII code 10). Files created with Windows text editors ,may also contain a CR (ASCII code 13) at the end of each line. This type of file is also acceptable to the program.

In order for a data file to be recognized by the RadioCtl program, the first record in the file MUST contain the characters: *radioctl .The '*' MUST start in the first column of this record. The characters can be lower, upper or mixed case. Any other characters after this identifier are ignored.

Most record types require a record ‘index’. This index uniquely identifies the record. A number of data records contain 'references' to other record indexes. If a reference is 0, or references an undefined record, then the record is referred to as an 'orphan' and may not be able to be utilized. If multiple files are loaded by the program, all valid index references are adjusted automatically to match any changes to the record indexes made by the program.

In general, the references are:
      FREQ->GROUP->SYSTEM
     TFREQ->SITE->SYSTEM
     BPLAN->SITE->SYSTEM.

A few record types do NOT reference other records. They include record types that are settings for the program or the radio.

 The record structure has been designed to be as general as possible. Some fields/keys defined may be applicable only to specific radios. In general, the program will ignore fields that are not used by the current radio being controlled. Also note that a number of fields are not included in the GUI databases.

In the descriptions that follow, required fields are identified for each record type. For positional records, all fields BEFORE these required fields MUST be included (even if they are blank). For non-positional records, any field NOT marked as required does not need to be set, and will assume some default value.
.

Notes on Uniden Quick-keys:
  Quick-key implementation on the BCD396, the BCD325P2 and the SDS200 are a bit different.
The BCD396 has 100 system quick-keys (1-100). Each group in a system can have a quick-key from 0 to 9.
The BCD325P2 has 100 system quick-keys (0-99). Each group in a system can have a quick-key from 0 to 9.
The SDS100 and SDS200 have 100 Favorites quick-keys (0-99) that select a favorites file for scanning. Each favorite has up to 100 system quick-keys (0-99) that are unique for that favorites list. Each System has up to 100 department (GROUP) quick-keys (0-99) that are unique for that System.
For RadioCtl, 'departments' are called 'groups'.
For trunked systems, the BCD325P2 ignores the SYSTEM quick-key setting and instead utilizes the quick-key defined in the SITE records.
The BCD396 does not have separate SITE records, so the SYSTEM quick-key is always used for both conventional and trunked systems.

The SDS100 and SDS200 treat quick-keys defined in SITE records as department keys. So these keys are shared between SITE and GROUP records. Care should be exercised so that the same quick-key is NOT assigned to both the SITE and GROUP in a single system. RadioCtl will allow this, but will warn the user if this is detected.

RadioCtl allows specification of QKEY fields of integers from -1 to 99, as well as ‘.’, ‘-’ or a blank. If the input value is NOT an integer between 0 and 99, the quick-key in the radio will be turned off. When storing a key into the BCD325P2 or BCD396 Radio’s GROUP memory, the value will be ‘mod 10’ of the value.
   Ex: RadioCtl GROUP QKEY value = 25, will be stored in the radio as 5.
For the BCD396, a SYSTEM QKEY value of 0 will store into the radio’s memory as 100.

A separate quick-key setting (‘dqkey’) is provided for both ‘SITE’ and ‘GROUP’ RadioCtl records. This key is ONLY used when generating SD Card data for SDSx00 radio. This setting is provided so that different keys can be defined for BCD and SDS radios using the same records.

When storing data into a Uniden Radio, or generating SD Card data for a Uniden radio. RadioCtl places some rules on quick-key definition:

1. All SYSTEM records must have a quick-key defined. If a quick-key is NOT defined, the system will not be stored, nor will the SD Card data be generated for that system.
2. All SITE records must also have a quick-key defined. As with the SYSTEM record, SITE records without a valid quick-key definition will be discarded.
3. GROUP records should have a quick-key defined. However, if one is not, the GROUP will still be used, but a warning message will be issued indicating that this group CANNOT be selected. For this situation, ‘LOUT’ (Lock-out) in the radio (or ‘Avoid’ in the SD card) will be turned ON.
4. For SYSTEM, SITE and GROUP record types, ‘LOUT’ in the radio (or ‘Avoid’ in the SD card) will not normally be set. Instead the quick-key defined will be turned on or off based on the ‘valid’ field in the record. If ‘valid’ is TRUE, the key will be turned on. Otherwise the key will be turned off. ‘_extra’ keys are defined to override this action.
5. When generating SD Card data for SDSx00 radios, only one ‘SYSTEM’ record (and children) per file will be generated. The Favorites quick-key will be set to the same value as the SYSTEM quick-key. If the ‘SYSTEM’ record has ‘valid’ set to TRUE, the ‘MONITOR’ setting in the favorites will also be turned on. Otherwise, ‘MONITOR’ will be turned off. An ‘_extra’ key is defined to override this action.

### Comment records
   Comments start with a '*' or a '#'. These records are ignored for most processing by both the GUI and the command line program. However, some comments that start with a '#' are treated specially.

If a valid record type is preceded with comment records that start with a '#', these records are kept with that record when the file is recreated. The rules for '#' records are as follows:
- There must be a '#' in the first column
- There must be NO blank lines, or lines that start with a '*' before the line that contains the record type.

An example:
   # This is a comment line. It will be recreated BEFORE the ‘freq’ record below
   # This Comment will also be recreated in the same place
   freq,10,Fire Dept,1,1, ..…

If a comment record starts with #:, then the record will define the fields for a positional record type. These comments are called FORMAT comments and are in the form:
      #:rectype:field1,field2,field3,...
where 'rectype' is the record type (FREQ, SYSTEM, etc) and each field specified is the keyword for each positional field. The record type, and the fields specified can be in Upper, Lower or Mixed case.
FORMAT comments allow the user to utilize files that may have been created with older versions of Radioctl.
Multiple FORMAT comments can be included in a single file. All records following the FORMAT comment will utilize that format for positional records until another FORMAT comment is encountered.
FORMAT comments do NOT affect records in KEYWORD=VALUE format.
WARNING: Adding (or changing) a FORMAT comment can cause strange results if the positional fields do NOT match the format fields!

### TAG Records
Tag records are special comments that can be inserted by the user. Tag records will be preserved when a data file is read and then re-written at the beginning of the file. Tag records are in the format
 *:tagname: some text
where 'tagname' is a pre-defined tag. Tag records MUST start in column 1 of the file. The tagname is NOT case sensitive. However it is recommended that it be in UPPER case for clarity. When a file with tags is updated, all tags (except for a few special ones) will be preserved.

Table 2: Tags
tag	description
*:SYSTEM:	Name of the system (usually as per RadioReference.com)
*:QUICKKEY:	Uniden Quick-key assignments for the system. Multiple quick-key tags can be present if the file contains more than one system. / Note: This tag is generated by the RadioCtl write subroutine and is not preserved if the file is reprocessed.
*:START:	Start of multi-line comments. Comments following this tag will be copied to any updates to the file.
*:END:	End of multi-line comments.

### SYSTEM Records
SYSTEM records define a particular system. There MUST be at LEAST one SYSTEM record in every data file. Any SITE & GROUP records that do not reference a valid SYSTEM record, will be marked as orphans. Any FREQ, BPLAN or TFREQ records that reference orphaned SITE or GROUP records will also be marked as orphans.

Uniden radios have the ability to store SYSTEM records. These radios also provide support for receiving TRUNKED radio systems. All other makes of supported radios do not. The RadioCtl GUI program makes use of SYSTEM records for various operations for all radios. The GUI will ignore any SYSTEM definitions for trunked systems.

Table 3: SYSTEM record
position	key	type	description
1	rectype	string	Record type. (SYSTEM) / Information about a given system. SITE, GROUP & FREQ records are associated with a SYSTEM record. / This is a required field.
2	index	integer	System number index. This number MUST be unique for all SYSTEM records in the file, and must be greater than 0. / This is a REQUIRED field. If missing or < 1 then this record will be discarded.
3	service	string	Description of the system. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio. / If not specified, will be set to ‘System n’, where ‘n’ is the SYSTEM record index
4	valid	binary	If 1 (True/On), the record is active. The RadioCtl GUI may utilize this field to indicate if the system should be used for scanning and searching. / This field also affects how the record and/or the system is stored in the radio. / If not specified, defaults to 0 (False/Off).
5	systemtype	string	type of system. For the GUI program, and all radios EXCEPT Uniden, only 'CNV' (conventional) types are recognized. All other types are considered trunked systems, and only supported by Uniden models. / Systemtype is NOT case sensitive. / This is a REQUIRED field. / Valid values for systemtype are: / systemtype Description / CNV Conventional system / LTR LTR trunked system / EDS EDACS Scat / EDW EDACS Wide / EDN EDACS Narrow / MOTS Motorola Standard / MOTP Motorola Sprinter / MOTC Motorola Custom (Needs BPLAN record) / TRBO Motorola Turbo (DMR) / DMR Single channel DMR / P25S P25 standard (Phase I or II) / P25F P25 single channel / P25X P25 X2 TDMA (SDS100/SDS200 only) / NXDN NXDN (SDS100/SDS200 only) / NXDNS NXDN Single Channel (SDS100/SDS200 only)
6	flags	flag	Binary settings. Most of the flags affect Uniden Radios, and are not used by the RadioCtl GUI. / Flag characters can be upper or lower case. / If the Flag char is not specified, then the value is 0 (Off) / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified as keyname=1 (where 'keyname' is the affected key). / Valid flag characters for SYSTEM records are: / character key meaning / A atten Attenuation is on for this system. / C call I_Call enabled (BCD396 only) / D idas For SDS100 & SDS200 radios, Use IDAS format for the TGID. Default is NEXEDGE. / F afs TGID format is AFS (nn-xxx) / H agc_digital AGC Digital is on / I id_search ID-Search is On / J agc_analog AGC Analog is on / K skip Data Skip is on. (BCD396 only) / O c_ch Control Channel Only (BCD396 only) / S s_bit Motorola status bit on / X moto_id P25 display in hex
7	dlyrsm	integer	Delay or Resume value. / A negative value indicates Resume. / A positive value indicates Delay. / 0 is off (Default if not specified). / This value MAY be adjusted when storing into a radio.
8	qkey	integer	The system quick-key for Uniden radios only. The value is a number between 0 and 99. A blank, ‘.’ or -1 indicates that this key is not to be set. / A value is required in this field if this is a conventional system type to be stored in a Uniden Radio. / NOTE: For Trunked systems, the BCD325P2 & BCD325 use the quick-key from the SITE record rather than the SYSTEM record internally. / However, the quick-key should ALWAYS be included in the system record, as the SDS100 & SDS200 WILL utilize the SYSTEM record rather than the SITE record. / Although this field is NOT required, if it is NOT set, the system may not be usable for Uniden Radios.
9	hld	integer	The time to hold on this system in seconds (0-255). / If not specified, defaults to 0.
10	(varies)	extra	Extra definitions for Uniden radios. These are usually numerical assignments. Each definition in this field is in the format: key=n ,where 'key’ is the key that the value is for, and 'n' is usually an integer. / Multiple extra definitions are separated by a space. / The following keys can be specified in this field: / key description / hpd For SDS100 and SDS200 radios, the index of the .hpd file that will be generated for the Favorites SD Card data. / RADIOWRITE will use this key for the ‘CSV2SDS’ command. / ex: HPD=5 will generate the file f_000005.hpd for this system. / If this value is not specified, file numbering will be sequential (starting with ‘f_000000.hpd’) for each SYSTEM record processed. / utag This is a user defined number for this system. The value must be an integer between 0 and 99. / If the value is less than 0, or not specified, then this field will be ignored. / emgalt Emergency Alert Tone. Value must be between 0 and 9. If 0, or not specified, the tone will be turned off. / emglvl Emergency Alert Volume. Value must be between 0 (off) and 15 (maximum). If not specified, value will default to 0 (Off). / emgpat Emergency Alert Pattern. This can be 0-On (default), 1-Slow Flash, or 2-Fast Flash. / turnqk Override for quick-key on or off. Value is On or Off (not case sensitive). / ex: turnqk=on #Forces the quick-key on regardless of the valid setting.
13	p25wait	integer	Time to wait in ms for a P25 decode. Value is between 0 and 1000. For the BCD Radios, the value must be in increments of 100. Recommended value is 400 for Digital Voice Systems (P25/DMR/Turbo). This is the default, if not specified. / NOTE: If P25wait is set to 0 for a digital system, the scanner MAY not stop on transmissions.
14	(reserved)	-	Reserved for future usage
15	p25lvl	integer	P25 'Digital Squelch' level. Values are 0-63. / For the SDSx00 radios, the values are 5-13. / When generating SDS SD card values, this value will be adjusted to be within the radio’s ranges. / If not set, will default to 5.
16	p25nac	hex	P25 Network Access code. Value is 0-1FF (hex) or ‘S’ for ‘Search’
17	end_code	character	A single character indicating the end code for a Motorola System. / Character can be: / ‘a’ - Analog. / ‘b’ - Analog+Digital / ‘I’ - Ignore (default)
18	fleetmap	integer	Motorola Fleet Map Selection. This is a number from 0-16. / 0-15 are pre-defined mappings. 16 identifies that a custom mapping will be used. That custom mapping is in field 18 (‘custmap’) of the SYSTEM record. This field is ONLY used by BCD radios when the system type is MOTC. / This field is not used by SDS radios.
19	custmap	hex	Motorola custom fleetmap. The value is 8 hex characters, 0-E (Hex ‘F’ is not allowed). Each digit position represents the size of each block (block 0 to block 7). / This field is ONLY used if the system type is MOTC. For BCD radios, field 17 (FLEETMAP) must also be 16 for this field to be utilized.

### SITE Records
Site records contain information on a specific trunked system location. Site records currently are only used by Uniden Dynamic Radios.
Any SITE records that do not reference a valid SYSTEM record, will be marked as orphans. Any TFREQ or BPLAN records that reference orphaned SITE record will also be marked as orphans.
Site records are NOT processed by the GUI version of RadioCtl.

Table 4: SITE Record Fields
position	key	type	description
1	rectype	string	Record type. (SITE) / Information for Trunking transmission sites. / This is a REQUIRED field.
2	index	integer	Site number index. This number MUST be unique for all SITE records in the file, and must be greater than 0. / This is a REQUIRED field. / If this index is less than one, then this record will discarded.
3	Service	string	Description of the Site. Uniden radios limit this to 16 characters. / NOTE: Site Service strings will be displayed on the radio rather than the SYSTEM service string. / If not set, the value will be “Site n” where ‘n’ is the index value.
4	Valid	binary	Determines the setting of the quick-key in the radio. If it is 1 (True/On), the quick-key (defined in this record) will be turned on in the radio. Otherwise the quick-key will be turned off. / If not specified, defaults to 0 (False/Off)
5	sysno	integer	System index number reference that this SITE is associated with. If this value is 0, or references a non-existent system number, then this record will be treated as an orphan, and any TFREQ or BPLAN records that reference it will also be considered orphaned. / This is a REQUIRED field.
6	qkey	integer	Uniden Quick-Key for this site. / When storing into the radio (or generating SD Card data), how this key is used will depend on the model. / Although this is NOT a required field, If this field is missing or less than 0, this SITE record cannot be stored in any radio.
7	hld	integer	Time in seconds to hold on this site when scanning. / If not specified, defaults to 0.
8	flags	flag	Flags for the record. Flag characters can be upper or lower case. / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified. / Valid Flag Characters are: / character key meaning / A atten Attenuation is on for this site. / O c_ch Control Channel Only (BCD325P2 only) / Z gps Enable GPS (BCD325P2 only)
9	mode	mode	Modulation. Valid values are AUTO, FMn, FMun. / If not specified, defaults to ‘FMn’.
10	lat	coord	Latitude of the site. IF DMS format, direction MUST be 'N' or 'S' / If not specified, defaults to 0
11	lon	coord	Longitude of the site. If DMS format, direction MUST be 'E' or 'W' / If not specified, defaults to 0
12	range	number	Number of miles for the range. Decimal number. (SDSx00 radio usage only). / If not specified, defaults to 25.
13	rf_filter	string	One or two characters identifying the filter to be used for SDS100/SDS200 only. Case of the character(s) is not significant. If not specified, defaults to ‘o’ (Off). / char Filter / n Normal / i Invert / a Auto / nw Normal Wide / iw Invert Wide / aw Auto Wide / o Off
15	site_number	string	This is an informational only field. The value is not checked or used by any RadioCtl process. This usually reflects the actual site information for this system.
16	(varies)	string	Extra definitions for Uniden radios. These are usually numerical assignments. Each definition in this field is in the format: key=n , where 'key’ is the key that the value is for, and 'n' is usually an integer. / Multiple extra definitions are separated by a space. / The following keys can be specified in this field: / key description / dqkey Department quick-key. For SDSx00 radios, this will override the ‘qkey’ value in this record. / The SITE quick-key for Uniden BCD radios is usually the same as the SYSTEM record. However, for SDSx00 radios, the SITE quick-key is shared with GROUP (‘Department’) quick-keys. / This optional field allows the same SITE record to be used in both BCD and SDS radios. / If this key is -1 or not specified, then the ‘qkey’ field will be used when setting SDS radio data. / turnqk Override for quick-key on or off. Value is On or Off (not case sensitive). / ex: turnqk=on #Forces the quick-key on regardless of the valid setting. / turndqk Override for Dept quick-key on or off. Value is On or Off (not case sensitive). Only used if dqkey is specified, and only when creating SDSx00 SD Card data.

### BPLAN Records
 Uniden radios provide for the ability to specify a custom band-plan for Motorola Systems. The radio will only make use of this record if systemtype is 'motoc'
position	key	type	description
1	rectype	string	Record type. (BPLAN) / Custom Motorola Band-Plan record. / This is a REQUIRED field.
2	index	integer	BPLAN number index. This number MUST be unique for all BPLAN records in the file, and must be greater than 0. / NOTE: Normally, There is only one BPLAN per site.
3	siteno	Integer	The site number that this record is for. If this value is 0, or / references a non-existent site, or the site referenced does not reference a valid system number, this record will be ignored.
4	flags	characters	Any flag characters for this record. / At this time, there are no valid flags defined for BPLAN records.
5	frequency_l1	frequency	Low frequency number 1. Value in Hz
6	frequency_h1	frequency	High frequency number 1. Value in Hz
7	spacing_1	frequency	Spacing number 1. Value in Hz
8	offset_1	integer	Offset number 1. Value is integer from -1023 to 1023
9	frequency_l2	frequency	Low frequency number 2. Value in Hz
10	frequency_h2	frequency	High frequency number 2. Value in Hz
11	spacing_2	frequency	Spacing number 2. Value in Hz
12	offset_2	integer	Offset number 2. Value is integer from -1023 to 1023
13	frequency_l3	frequency	Low frequency number 3. Value in Hz
14	frequency_h3	frequency	High frequency number 3. Value in Hz
16	spacing_3	frequency	Spacing number 3. Value in Hz
17	offset_3	integer	offset number 3. Value is integer from -1023 to 1023
18	frequency_l4	frequency	Low frequency number 4. Value in Hz
19	frequency_h4	frequency	High frequency number 4. Value in Hz
20	spacing_4	frequency	Spacing number 4. Value in Hz
21	offset_4	integer	Offset number 4. Value is integer from -1023 to 1023
22	frequency_l5	frequency	Low frequency number 5. Value in Hz
23	frequency_h5	frequency	High frequency number 5. Value in Hz
24	spacing_5	frequency	Spacing number 5. Value in Hz
25	offset_5	integer	Offset number 5. Value is integer from -1023 to 1023
26	frequency_l6	frequency	Low frequency number 6. Value in Hz
27	frequency_h6	frequency	High frequency number 6. Value in Hz
28	spacing_6	frequency	Spacing number 6. Value in Hz
29	offset_6	integer	Offset number 6. Value is integer from -1023 to 1023

### TFREQ records
 For each site defined, there should be frequencies for that site. These records identify those frequencies used. TFREQ records are ONLY used for trunked systems. Conventional systems use 'FREQ' records.

Table 5: TFREQ record fields
position	key	type	description
1	rectype	string	Record type. (TFREQ) / Frequencies for a given SITE / This is a REQUIRED field.
2	index	integer	Site number index. This number MUST be unique for all SITE records in the file, and must be greater than 0. If index is 0, then the record will be discarded. / This is a REQUIRED field.
3	valid	binary	If set to FALSE, this site will be locked-out. / Defaults to TRUE.
4	siteno	integer	Reference to the site number this frequency is for. If the value is 0, the siteno referenced does not exist, or the siteno referenced does not reference a valid system, this record will be discarded.
5	frequency	frequency	Frequency in Hz or MHz. If a decimal point is present, the value is assumed to be in MHz. The frequency must not be 0. TFREQ records with a 0 frequency will be marked not valid and ignored.
6	lcn	number	LCN for this frequency. Not all trunked systems use LCN numbers. / If no LCN, the value can be blank, 0 or '-'. Maximum LCN number is 4096
7	mode	modulation	Only 'FMn, or 'FMun' are acceptable for trunked frequencies. / If not given, defaults to ‘FMn’
8	ccode	number	Color Code for DMR systems. Value can be 0-15, or ‘s’, indicating ‘search’. / If not given ‘s’ is default. / This field is only used if the system type is DMR or TRBO.
9	ran	number	Radio Access Number for NXDN systems. The value can be 0-69 or ‘s’ indicating ‘search’. / If not given ‘s’ is default. / This field is only used if the system type is NXDN or NXDNS.
10	utag	number	This is a number that the user can assign to a Trunked Frequency as an ID. The value in this field is 0-999. If The value is blank or less than 0, then the tag will not be used.
11	flags	flag	Flags for the record. / Flag characters can be upper or lower case. / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified. / At present, no flags are defined for the TFREQ record.
12	_extra	-	Extra field definitions. / For now, there are no extra keys defined for the TFREQ record.

### GROUP Records
  GROUP records identify frequencies that have some common grouping. For example, a group might be created called FIRE which identifies all frequencies associated with Fire Departments. The RadioCtl GUI allows for scanning by these GROUP records.
Uniden Dynamic Radios also allow for processing and storing group information. These radios can save up to 20 groups assigned to a system. In order for any GROUP record to be stored in a Uniden radio, it MUST be associated with a SYSTEM record. The RadioCtl GUI has no restrictions on the number of GROUP records, or requirement of SYSTEM linkage.

The some ICOM radios also utilize group records. However, at the current time, there is no way to directly read or write these values. If ICOM updates the firmware in these radios, this situation may change. Group information in ICOM radios CAN be written to an SD card, if the radio supports it. Using SD card data, Group information can be stored in these radios.

All other radios do not have the ability to store GROUP information.

 Table 6: GROUP Record Fields
position	key	type	description
1	rectype	string	Record type. (GROUP). / Categories of the various services that the radio may receive. / This is a REQUIRED field.
2	index	integer	Group number index. This number MUST be unique for all Group records in the file, and must be greater than 0. If this value is 0, the record will be discard. / This is a REQUIRED field.
3	service	string	Description of the group. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio. / If not specified, this value will be set to ‘Group-x’, where ‘x’ is the Index field value.
4	valid	binary	If TRUE, the Group will be used by the program and by the radio (if the radio supports it). If FALSE, the group will be locked-out in the radio (and in the GUI). / Note: When storing into Uniden BCD radios, the VALID flag will determine if the GROUP quick-key is set on or not. For these radios, a defined group is never locked-out.
5	sysno	integer	System index number that this GROUP is part of. / If this value is 0, or references a non-existent system number, then this record will be marked as an orphan.
6	flags	character	Flags for the record. / For keyword=value format, the flag field is NOT used. Instead the individual key is specified. / Currently there are no valid flags defined for this record type.
7	(none)	(none)	Reserved field for future enhancements
8	(varies)	string	Extra definitions for this record. The extra field values are in the format key=value. / These are values that are specific for certain radios. / key description / scangrp Scan group for ICOM IC-705 & IC-8600 radios. / For the IC-705 The value must be 1-3. For The IC-8600, the value must be 1-9. / If the value is greater than 0, then this will be the default scan group set when a ‘FREQ’ record does not contain a ‘scangrp’ value, or that value is < 1. / This key is not used by any other radios. / svcode Service code for Uniden SDS radios. The value must be between 1-37 (pre-defined codes) and 208-206 (custom codes). / dqkey Department quick-key. For SDSx00 radios, this will override the ‘qkey’ value in this record. / For SDSx00 radios, the GROUP quick-key is shared with SITE (‘Department’) quick-keys. / This optional field allows the same GROUP record to be used in both BCD and SDS radios. / If this key is -1 or not specified, then the ‘qkey’ field will be used when setting SDS radio data. / turnqk Override for quick-key on or off. Value is On or Off (not case sensitive). / ex: turnqk=on #Forces the quick-key on regardless of the valid setting. / turndqk Override for Dept quick-key on or off. Value is On or Off (not case sensitive). Only used if dqkey is specified, and only when creating SDSx00 SD Card data.
9	gqkey	integer	Uniden Group Quick-key (0-9). Although not required, A quick-key should ALWAYS be defined for Uniden radios, or the group can never be de-selected.
10	rf_filter	string	One or two characters identifying the filter to be used for SDS100/SDS200 only. Case of the character(s) is not significant. If not specified, defaults to ‘o’ (Off). / char Filter / n Normal / i Invert / a Auto / nw Normal Wide / iw Invert Wide / aw Auto Wide / o Off
11	lat	coord	Latitude of the group. If DMS format, direction MUST be 'N' or 'S'
12	lon	number	Longitude of the group. If DMS format, direction MUST be 'E' or "W'
13	range	number	Number of miles for the range. Decimal number. (SDS100/SDS200 only)

### FREQ records
 FREQ records define individual frequencies or trunk ids (TGID). The records include Modulation, service and other information that MAY be stored in a radio's memory channel. These records are also used by the RadioCtl GUI program.
If the record defines a Trunked Group ID (TGID), the frequency value should be 0. A 0 frequency for a record that does NOT contain a valid TGID is assumed to be a blank channel. TGIDs are only stored to and fetched from Uniden Radios.

Table 7: FREQ Record Fields
position	key	type	description
1	rectype	string	Record type. (FREQ). / Frequency and other information used by both The RadioCtl program and stored in the radio's memory.
2	index	integer	Freq number index. This number MUST be unique for all FREQ records in the file, and must be greater than 0. / If this value is 0, this record is discarded.
3	service	string	Description of the Frequency. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio.
4	valid	binary	If TRUE, the Frequency will be marked for scanning and selection by the RadioCtl GUI and by the radio.
5	groupno	integer	GROUP index number that this FREQ record is part of. / If this number is 0, or references a non-existent group index, or the referenced group does not reference a valid SYSTEM record, then this record will be orphaned.
6	flags	character	Single character flags indicating some attribute of this record. Characters are NOT case sensitive. Multiple flags can be specified. / Note that some radios have the ability to store attenuation in the radio's memory channels. For these radios, there is a separate attenuation flag. / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified. (ex: ATTEN=1) / Valid flag characters are: / char key meaning / A atten Attenuation is on for this frequency for ALL radios. / 2 sdaatt Attenuation is on if this is a Uniden SDS100 or SDS200 model radio. / 3 bcdatt Attenuation is on if this is a Uniden BCD325P2 or BCD396 model radio. / 4 r30att Attenuation is on if this is a ICOM IC-R30 model radio. / G tgid_valid This is a TGID (Trunked Group ID). Only affects Trunked systems. / For keyword=value format, this flag is assumed if the value of TGID is set. / P priority Priority is on / + oplus Positive offset. ICOM/Kenwood Radios only / < ominus Negative offset, ICOM/Kenwood Radios only
7	channel	integer	Channel number for the radio. Valid values are 0 thru 9999, -1, ‘-’ , ‘.’ or blank. / If the value is not a number between 0 and 9999, the record MAY be ignored for certain operations. / If the value is outside of the radio’s range, the record will also be ignored. / NOTE:For certain ICOM radios, the channel number represents two parts: The Group and the Channel in that group. For these radios, the last two digits are the Group and the first two are the channel in that group. / EX: Channel 1234 would be ICOM group 12, channel 34.
8	frequency	frequency	Frequency in Hz or MHz. If a decimal point is present, the value is assumed to be in MHz. The frequency should NOT be 0 unless this is a TGID record, or the radio's channel is to be cleared.
9	mode	mode	Modulation string. Acceptable values are AM, FM, FMw, FMn, FMun,LSB, USB, AUTO and possibly others (depending on the radio). Case of the string is not important. If AUTO is specified, RadioCtl (or the radio) will attempt to adjust the modulation based on the Frequency. Note that some radios do not allow all modulations, or cannot change the modulation. This field is ignored if this is a TGID record.
10	tgid	tgid	Trunked Group ID. If the 'G' freq_flag is set, this field will be used for Uniden Radios only. A TGID record ignores the FREQUENCY and MODE fields.
11	tone	decimal or hex	A decimal number indicating the sub-audio tone, or digital ID used for squelch or repeater operation. Tones can be CTCSS (67.0 to 254.1) or DCS (023 to 754), as well as P25 NAC (0-FFFx), DMR Color Code (0-15), and NDXN RAN (0-63) values. The value can also be 'off' or 0 indicating no tone used. / If the specified tone does NOT exactly matched the predefined values, the program will attempt to match to the correct value. / What the tone represents is determined by the TONE_TYPE field. / NOTE: Not all radios have the ability to utilize sub-audio tones or IDs.
12	tone_type	string	Type of tone that the 'tone' field represents. This field is NOT case sensitive. The tone type MUST be compatible with the audio type specified in the 'adtype' field of this record. / In order for tone processing to be valid, the 'mode' MUST be ''FM', 'FMn', or 'FMun'. / Valid values are: / value meaning / Off Tone is off, Tone field is ignored / CTCSS The Tone field is a CTCSS frequency. Tone is used to squelch unless the CTCSS tone value is being transmitted. / CTCSS tone squelch can be set in the GUI. / DCS The Tone field is a DCS code. Tone is used to squelch unless the code is transmitted. / If the DCS code is > 999, then the 'Reverse' indicator in the radio will be set. / This ONLY applies to the ICOM IC-R30. This indicator is ignored for all other radios. / DCS squelch can be set in the GUI. / RPTR The tone field is a Repeater keying tone. The radio will add the tone to any transmissions. (IC-703 & Kenwood only). / RPTR tone is not available in the GUI. / NAC The tone is a DCR NAC value. The squelch will not break until the P25 NAC is recognized. / The 'tone' field is assumed to be in HEX. / This is only used with P25 systems, and not available in the GUI / CCODE The Tone field is a DMR Color Code. The squelch will not break until the DMR Color code is recognized. / This is only used for DMR type systems, and not available in the GUI / RAN The Tone field is a NXDN RAN value. / The 'adtype' field MUST be 'NXDN' or 'NXDNVN'. The system type must also be NXDN. RAN is not available in the GUI.
13	dlyrsm	integer	Delay or Resume value. / -10, -5 -2 indicates Resume. / 1 to 30 indicates delay. / 0 is off. / Used by the GUI and some radios.
14	(varies)	string	Extra definitions for this record. These are values that are specific to certain radios. / The extra field values are in the format key=value. / key Description / emgalt Emergency Alert Tone. 1-9. If 0, Emergency alert is turned off. / Uniden radios only. / emglvl Emergency Alert Volume Level 1-15, If 0, Emergency alert is turned off / emgpat Emergency Alert Pattern. 0-ON, 1-Slow flash, 2-Fast flash / rfgain For the ICOM R30 only, this is the value of the RFGAIN setting. This value must be between 0 and 9. If value is 0, or not set, RFGAIN will be set to RFMAX. / scangrp Scan group for ICOM radios. Value can be 0-9. / This is an indicator that the channel is to be included in a Select Memory Scan. / For the IC-705 The value must be 0-3. For The IC-8600, the value must be 0-9. / A value of 0 indicates that the channel will NOT be included in any scan group. / This value overrides any value set in the associated GROUP record. / svccode Service code (1-37,208-216). Only used by the Uniden SDS100/SDS200 / Note that the SDS radios MUST have a service code set in the channel, or the channel will NOT be included in scanning, / voloff Volume offset for Uniden Radios. This value is an integer between -3 and +3. The default value is 0.
15	adtype	string	Audio type. This field affects how an audio signal is processed by the radio. It also affects what 'tone_type' can be used for squelch processing. / Valid values are: / value usage / ALL Type of audio will be determined by the radio, and the 'tone_type' field. / This is valid for ALL radios. / ANALOG Only Analog voice/tone processing is done. / This is valid for ALL radios. / DIGITAL Only digital voice/tone processing is done. / NXDN The audio is an NXDN-N (12kHz) digital signal. / NXDNVN The audio is an NXDN-VN (6kHz) digital signal. / P25 The audio is a P25 digital signal. / DMR The audio is a DMR digital signal / DSTAR The audio is a D-Star Digital signal.
16	lat	coord	Latitude of the transmitter for this frequency. Can be entered in decimal or DMS (dd:mm:ss.ss:direction). Only used when creating records for the ICOM IC-R30 SD card. If '0' or '', this field is not set.
17	lon	coord	Longitude of the transmitter for this frequency. Can be entered in decimal or DMS (dd:mm:ss.ss:direction). Only used when creating records for the ICOM IC-R30 SD card. If '0' or '', this field is not set.
18	(reserved)	-	Reserved for future changes
19	sfrequency	frequency	Split or offset frequency in Hz or MHz. If 0, or the frequency is the same as the main frequency, (Field 8). no split frequency is indicated. / If the oplus (+) or ominus (-) flags are indicated, this will be treated as an offset frequency. / Split frequency or offset usage is ONLY appropriate for models that can transmit (ICOM IC-705, ICOM IC-703 and Kenwood TH-F6A). / However, The ICOM IC-R30 will recognize offset usage ONLY when writing to the SD-Card.
20	smode	mode	Split modulation. If specified, identifies a modulation for a split channel to be stored to or retrieved from the radio. If SFREQUENCY given, but SMODE is not, the modulation specified in the MODE field will be used. SFREQUENCY must be specified for SMODE to be processed.
21	stone	decimal	Split tone. If specified, and is not 0, it identifies a tone (CTCSS/DCS/REPEATER) for a split channel to be stored to or retrieved from the radio. If SFREQUENCY given, but STONE is not, the tone specified in the TONE field will be used. SFREQUENCY must be specified for STONE to be processed.
22	stone_type	string	Split tone type. If specified, and is not 'off', this will identify a tone type (CTCSS/DCS/REPEATER) for a split channel to be stored to or retrieved from the radio. If SFREQUENCY given, but STONE_TYPE is not, the tone specified in the TONE_TYPE field will be used. SFREQUENCY must be specified for STONE_TYPE to be processed.

Split frequencies or offsets are used by radios that allow for transmission (on Ham Bands), as well as reception by the ICOM R30. These splits are defined using ONE of these methods:
- '+' or '-' for the flag value and a frequency offset for the sfrequency value. The offset MUST be greater than 100 kHz and less than 100 MHz.
  EX: ominus=TRUE,sfrequency=.6, frequency=146.61
- No '+' or '-' specified for the flag, and an sfrequency value different than the frequency value. The difference between the frequency and the sfrequency must be greater than 100 kHz and less than 100 MHz.
  Examples: frequency=442.0, sfrequency=447.0
  frequency=442.0,oplus=TRUE

Note that the ICOM R30 only supports offset specification. If the second format is specified when creating the SD Card output for this radio, the offset value will be calculated.

The Kenwood TH-F6A only uses split frequencies. If the offset format is specified for this radio, RadioCtl will calculate out what the split frequency should be when storing the record into the Radio's memory.

Audio type and tone type specifications require a number of rules to be followed.
- Only one tone type per FREQ is allowed
- The Tone-Type must be consistent with the Audio-Type
- Digital audio/tone types are only valid for certain radios.
- Digital audio/tone types are NOT supported on the GUI panels.

Table 8: Audio/Tone consistency chart
audio-type	allowed tone-type	Radios supported
ALL	Any	All
DIGITAL	RAN,NAC,CCODE	ICOM-R30 / UNIDEN BCD325P2 / UNIDEN SDS100 / UNIDEN SDS200
ANALOG	CTCSS, DCS, RPTR	All except ICOM R7000.. / RPTR is only for ICOM IC-705/Kenwood TH-F6A
NXDN, NXDNVN	RAN	ICOM-R30 / UNIDEN SDS100 / UNIDEN SDS200
P25	NAC	ICOM-R30 / UNIDEN SDS100 / UNIDEN SDS200 / UNIDEN BCD325P2
DMR	CCODE	UNIDEN SDS100 / UNIDEN SDS200 / UNIDEN BCD325P2
DSTAR	DSQL	ICOM-R30

The table below shows the SVCODE values used by Uniden SDS100 & SDS200. These codes can be specified in GROUP and FREQ records for use in building SD Cards for these radios.

Table 9: SVCODEs used By Uniden SDS Radios
Code	Meaning
1	Multi-Dispatch
2	Law Dispatch
3	Fire Dispatch
4	EMS Dispatch
5	(not assigned)
6	Multi-Tac
7	Law Tac
8	Fire-Tac
9	EMS-Tac
10	(not assigned)
11	Interop
12	Hospital
13	Ham
14	Public Works
15	Aircraft
16	Federal
17	Business
18	(not assigned)
19	(not assigned)
20	Railroad
21	Other
22	Multi-Talk
23	Law Talk
24	Fire-Talk
25	EMS-Talk
26	Transportation
27	(not assigned)
28	(not assigned)
29	Emergency Ops
30	Military
31	Media
32	Schools
33	Security
34	Utilities
35	(not assigned)
36	(not assigned)
37	Corrections
38-207	(Not valid in the radio)
208	Custom 1
209	Custom 2
210	Custom 3
211	Custom 4
212	Custom 5
213	Custom 6
214	Custom 7
215	Custom 8
216	Racing Officials

### SEARCH records
 Search records are used for setting Uniden BCD radio search memories. The STORE command in the RADIOWRITE program provides an option to include these records when storing into the radio.
The GUI program can also make use of these records for SEARCH operations.

There are two sets of search memory channels in the BCD325P2 & BCD396T. There are 13 ‘Service’ channels numbered 1-15. The BCD396T only supports 12. Channel 10 is Not defined on the BCD325P2.
Channel 15 is Not defined on the BCD396T. Channels 13 & 14 are not defined for either radio.

The Uniden Radios provide the ability to do search while scanning. Each search channel can run when the radio is doing normal scanning. There are two settings that enable this to happen: The ‘Lock-Out’ setting (set by the ‘Valid’ field) and the state of the quick-key defined in the search memory.

Table 10: Search While Scan actions
Lock-out	Quick-key	Action
On	On/Off/Not Defined	Search record will not run during scan
Off	Off	Search record will not run during scan
Off	On	Search record Will run during scan
Off	Not Defined	Search record will ALWAYS run during scan (cannot be turned off)

 NOTE: The quick-keys used for SEARCH are the same keys used for each System stored in the radio. To prevent confusing situations, Search quick-key numbers should be chosen to be DIFFERENT from System keys.

Table 11: SEARCH record fields
position	key	type	description
1	rectype	string	Record type. (SEARCH).
2	index	integer	Search number index. This number MUST be unique for all SEARCH records in the file, and must be greater than 0. / If this value is 0, this record is discarded.
3	valid	binary	Turns on or off this search. If it is 1 (True/On), this search will be enabled. / For Search records, this translates to the inverse of the ‘Lock-Out’ setting in the radio. If Valid is 1, ‘Lock-Out’ is 0, else ‘Lock-Out’ is 1. / If valid is not specified, defaults to 0 (False/Off)
4	service	string	Description of the search. Any valid text can be used. Although there is no limit to the length of the text for RadioCtl, the text may be truncated to a specific length when stored in a radio. / This field is only used when storing into CUSTOM search memories.
5	start_freq	frequency	First Frequency in Hz or MHz. If a decimal point is present, the value is assumed to be in MHz. / This field is only used when storing into CUSTOM search memories.
6	end_freq	frequency	Last Frequency in Hz or MHz. If a decimal point is present, the value is assumed to be in MHz. / This field is only used when storing into CUSTOM search memories.
7	step	frequency	Step Frequency in Hz or MHz. If a decimal point is present, the value is assumed to be in MHz. / This field is only used when storing into CUSTOM search memories.
8	mode	mode	Modulation string. Acceptable values are AM, FM, FMw, FMn, FMun, AUTO Case of the string is not important. This field is only used when storing into CUSTOM search memories.
9	flags	character	Single character flags indicating some attribute of this record. Characters are NOT case sensitive. Multiple flags can be specified. / For KEYWORD=VALUE format, the flag field is NOT used. Instead the individual key is specified. (ex: ATTEN=1) / Valid flag characters are: / char key meaning / A atten Attenuation is on for this search. / H agc_digital AGC Digital is on32 / J agc_analog AGC Analog is on
10	_extra	-	Extra definitions for Uniden radios. These are usually numerical assignments. Each definition in this field is in the format: key=n , where 'key’ is the key that the value is for, and 'n' is usually an integer. / Currently, there are NO extra field definitions for this record.
11	dlyrsm	integer	Delay or Resume value. / -10, -5 -2 indicates Resume (BCD325P2 only) / 1,2,5, 10 or 30 indicates delay. (BCD396T only uses 1-5) / 0 is off.
12	hld	integer	Time in seconds to hold on this search when scanning. / If not specified, defaults to 0.
13	p25wait	integer	Time to wait in ms for a P25 decode. Value is between 0 and 1000 in increments of 100. Recommended value is 400 for Digital Voice (P25/DMR/Turbo). This is the default, if not specified. / NOTE: If P25wait is set to 0 for a digital frequency, the scanner MAY not stop on transmissions.
14	srch_ndx	Character	Index for the search memory. This is specified as ‘Cx’ or ‘Sxx’. ‘C’ indicates the Custom channel, with ‘x’ being 0-9. ‘S’ indicates the Service channel, with ‘xx’ being 0-15. ‘S’ and ‘C’ can be upper or lower case. / If the channel is not supported by the radio, then there will be an error message displayed when attempting to store the record. / Examples: / c7 - Record will be stored in Custom channel 7 / s11 - Record will be stored in Service channel 11
15	qkey	integer	Quick-key to assign to this search record. Value can be 0-99, -1,‘.’, blank or ‘Off’. If not a number between 0 & 99, the quick-key will be unassigned. / If a quick-key is NOT defined for a search record, search with scan is enabled or disabled by the ‘Valid’ field only.
16	utag	Integer	This is a user defined number for this search. The value must be an integer between 0 and 999. / If the value is less than 0, or not specified, then the utag value will not be set.

### POWERMSG record
  This is a single record that defines the power on message for the radio. Only a small number of radios (Uniden and Kenwood) allow for setting a power on message.
Only one POWERMSG record is used. If multiple are found in a file (or group of files) the last one read will be the one used.
The POWERMSG record is typically specified using KEY=VALUE format. However, positional format is also acceptable.
Any key that is not specified will default to a blank line.
Table 12: POWERMSG Record Fields
position	key	type	description
1	rectype	string	Record type. (POWERMSG).
2	msg1	string	First line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.
3	msg2	string	Second line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.
4	msg3	string	Third line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.
5	msg3	string	Fourth line of the power on message. Although any length of string can be specified, the value for the radio will be limited by the number of characters that the radio recognizes.

### LIGHT records
This is a single record that defines the behavior of the back-light for the radio. Only a small number of radios (Uniden and Kenwood) allow for setting back-light behavior
Only one LIGHT record is used. If multiple are found in a file (or group of files) the last one read will be the one used.
The LIGHT record is typically specified using KEY=VALUE format. However, positional format is also acceptable.

Table 13: LIGHT Record format
position	key	type	description
1	rectype	string	Record type. (LIGHT).
2	event	string	When to turn on the light. Values are: / value description / ON Light is always on / OFF Light is always off / KEY / KY Light goes on briefly when a key is pressed (Uniden Only) / SQ Light goes on when there is a signal (Uniden Only) / 10 Light goes on for 10 seconds when the LIGHT key is pressed (Uniden only) / 30 Light goes on for 30 seconds when the LIGHT key is pressed (Uniden only)
3	bright	number	Brightness (1,2 or 3). Uniden only. / If not specified, defaults to 1.

### BEEP records
This is a single record that defines the volume of the key-press 'Beep'. Not all radios have the ability to set this value. For some radios (such as the Kenwood), the key-press sound is only on or off.
Only one BEEP record is used. If multiple are found in a file (or group of files) the last one read will be the one used.
The BEEP record is typically specified using KEY=VALUE format. However, positional format is also acceptable.

Table 14: BEEP Record format
position	key	type	description
1	rectype	string	Record type. (BEEP).
2	volume	number	Volume of the 'Beep'. Value is 0 (off), 1-15 (15 is the loudest). / If a value of 16 (or greater) is given for the BCD325P2, then 'Auto' will be set in the radio. For all other radios, anything > 15 will be considered maximum. / For radios without the ability of variable volume level, any value greater than 0 will turn ON the Beep.

### LOCKFREQ records
  These records are strictly for Uniden radios. They indicate a frequency that is locked out from scan or search. These records are NOT used by the RadioCtl GUI program.
Table 15: LOCKFREQ record fields
position	key	type	description
1	rectype	string	Record type. (LOCKFREQ).
2	frequency	frequency	The frequency (Hz or MHz) that is locked out

### IFXCHNG records
   These records are strictly for Uniden radios. They indicate a frequency that will have a different IF (Intermediate frequency) to eliminate 'birdies'. These records are NOT used by the RadioCtl GUI program.
Table 16: IFXCHNG record fields
position	key	type	description
1	rectype	string	Record type. (IFXCHNG).
2	frequency	frequency	The frequency (Hz or MHz) that is exchanged

### LOOKUP records
  LOOKUP records are used to identify known frequencies. These records are used only by the RadioCtl GUI program. They are not stored in any radio.
Table 17: LOOKUP record fields
position	key	type	description
1	rectype	string	Record type. (LOOKUP).
2	frequency	frequency	The frequency (Hz or MHz) for this assignment. Every frequency in this file should be unique. If there are multiple entries with the same frequency, the program will only make use of the first one found in the file.
3	service	string	Description of the usage of this Frequency. Any valid text can be used. There is no limit on the length of this value. However, if the string gets assigned to a variable that may be stored in a radio, that radio MAY limit the length.

### TONEOUT Records
   TONEOUT records are used exclusively for Uniden Radios. They define Tone-Outs that are stored in the radio for use with local fire and ambulance services. TONEOUT records can be stored in BCD radio memories (BCD396T/BCD325P2) using the TONEOUT command of RadioWrite. They can also be saved to the SD-Card for the SDS100/SDS200.

Although this table indicates the position of each field in a record, TONEOUT records are usually kept in KEYWORD=VALUE format.

position	key	type	description
1	rectype	string	Record type. (TONEOUT) / Tone-out setting
2	index	integer	number index. This number MUST be unique for all TONEOUT records in the file, and must be greater than 0.
3	service	string	The name of the Tone-Out. Any number of characters can be entered, but the radio will limit it to 16 characters
4	channel	integer	Tone-Out channel. For the BCD radios, this must be a number between 0 and 9 (representing Tone-Out settings 1-10). / For SDS radios, the number can be between 0 and 99.
5	frequency	frequency	The frequency (Hz or MHz) used by this agency. If a decimal point is included in the value, it is assumed to be in MHz.
6	mode	mode	Modulation string. Acceptable values are FM, FMn, or AUTO. / Any other modulation will be rejected by the radio.
7	toneout_a	frequency	The first tone value. This is specified in Hz. / The value must be 0, 250.0 to 3500.0.
8	toneout_b	frequency	The second tone value. This is specified in Hz. / The value must be 0, 250.0 to 3500.0.
9	flags	character	Single character flags indicating some attribute of this record. Characters are NOT case sensitive. Multiple flags can be specified. / For KEY=VALUE format, the flag field is NOT used. Instead the individual key is specified. (ex: ATTEN=1) / Valid flag characters are: / char key meaning / A atten Attenuation is on for this Tone-Out / J agc_analog AGC Analog is on. (Not used on BCD396T)
10	dlyrsm	integer	Specific values are 0 (no delay), 1,2,3,4,5,10,30. Any values greater than 30 will set the delay to 'Infinite'.
11	emgalt	integer	Alert Tone. 1-9. If 0, Emergency alert is turned off.
12	emglvl	integer	Alert Volume Level 1-15, If 0, Emergency alert is turned off
13	emgpat	integer	Alert Pattern. 0-On, 1-Slow, 2-Fast (not used on BCD396T)
14	emgcol	integer	Alert Color, 0 - Off, 1-Red. (not used on BCD396T) / NOTE:The SDS radios allow for colors other than RED. Numbers between 2 & 9 will translate to these colors when used by the SDS Radios. For the BCD325P2, numbers > 1 will translate to 1.

# Log File
The RadioCtl GUI can save activity information when scanning or searching. This includes frequency, signal strength, duration of signal, and a time stamp. The information is saved in a separate, comma delimited ('CSV') file. The directory where this file is placed is defined in the configuration file. The name of the file is set in the Operation Options panel on the Main window. If the 'Log Events' on this panel is checked, information is saved in this file. Records will be logged ONLY during scan or search operations, unless
the 'Update database in Manual' option is also selected.

Any filename can be specified. If the file specified does NOT exist, it will be created when the first log record is saved. If it DOES exist, each log record will be appended to the existing file. When a file is first created, the first record will indicate the field names.

Each record in the log file is a number of fields, each separated by a comma (','). This file can be viewed using any text editor, or imported into a spreadsheet program.

Table 18: Log File Records
position	description
1	Time Stamp. Human readable data/time for the log entry
2	Received Frequency in MHz
3	Modulation of the signal
4	Duration in seconds that a signal was detected
5	RadioCtl signal level (0-9)
6	RSSI (Received Signal Strength Indicator) if available. Not all radios return a RSSI indicator.
7	Channel number (if available). For dynamic radios, this may be blank
8	Service (if available)

# Configuration File
The configuration file is always named radioctl.conf. This file is used to configure the various radios that are used in the program, as well as some defaults. The file MUST reside in the home directory of the user. All radios that are to be utilized by RadioCtl must be defined in this file.
The format of each record of the file is:
   record_type,keyword=value,keyword=value, ....
There should be NO space between the keyword, '=' and value. As with data files, any record that starts with '*' or '#' is ignored. The record-type is NOT case sensitive, nor are the 'keyword's. Each keyword/value can be specified in any order. Any value missing will be set to the default UNLESS the keyword is required. If a required keyword is missing on a record, the program will terminate with an error message.
Important: Because of the way that configuration records are processed, no value can contain a comma (',') an equal sign ('=') or a '#';

### RADIO record type
This record type starts the definition for a radio. Any radio that is to be used by RadioCtl (GUI or Command line) MUST be defined with a RADIO record.

The following keywords are recognized:

keyword	Description
Name	Name of the radio. Any combination of alpha-numeric characters is allowed for the name EXCEPT ',' (comma) '=' (equal sign) or '#'. / The name MUST be unique. The name is NOT case sensitive so 'Bearcat' and 'BEARCAT' will be the same radio. / This is a required key. If this key is missing, then the program will terminate.
Protocol	The protocol for the radio. Must be one of the following: / protocol Radio models / Local Simulated radio. By default, one simulated radio is defined in the GUI. / Bearcat BC895XLT / Kenwood TH-F6A / Uniden BCD325P2, BCD396xlt, SDS100, SDS200 / Icom R-7000,IC-703,IC-R30 / AOR8000 AOR8000 / The protocol value is NOT case sensitive. Note that the models above are the ones that have been tested. Other models of the make of the radio MAY also work. / Protocol is a required key. If this key is missing, then the program will terminate.
Model	Model name. This value MUST be specified.
radioaddr	For ICOM radios only, this is a 1 byte hex value that the radio uses to identify commands that are for that radio. If not specified, the program will attempt to set this address based on the Model specified. If this address and the model are missing from this record, then the default address will be set to '08'x (R-7000 default address).
sdir	For radios with SD cards (ICOM R30, Uniden SDS200), this will be a directory for storing files that are destined for that Radio's SD card. This directory is used with the CSV2SDS and CSV2R30 commands. If not specified, the output will be stored in the default output directory, or the directory specified for those commands.

### DIRECTORY Record Type
This record defines the defaults for various directories used in the program. If a value is not defined in the configuration file, the default directory will be ~/radioctl

Table 19: DIRECTORY record type keys
keyword	Description
recdir	Directory to hold any recordings (.wav files).
tempdir	Default directory for most output files.
logdir	Directory to hold any log files.

### LOCATION Record Type
This record type defines a particular location that may be used in the program. A default location 'Home' is defined by RadioCtl. This can be overridden by specifying a 'Home' location in the configuration files. For some operations involving GPS coordinates, the coordinates can be specified using the name of the coordinates as defined in the configuration file.
NOTE:All keywords listed MUST be present (and valid) or the LOCATION record will be discarded.

keyword	Description
name	Name of this location. The case of the name is not significant. Ex: mine or Mine will be the same location. / If the name is 'Home', this will be used as the default location wherever coordinates are needed, but are not specified.
lat	Latitude of this location. Value can be Decimal (ex:46.1234) or DMS (ex:80:14:33.1:N). / Case of the direction in DMS is not significant ('n' is the same as 'N'). For DMS direction MUST be 'N' or 'S'. A negative decimal indicates 'S'.
lon	Longitude of this location. Value can be Decimal (ex:-75.1234) or DMS (ex:73:14:33.1:W). / Case of the direction in DMS is not significant ('w' is the same as 'W'). For DMS direction MUST be 'E' or 'W'. A negative decimal indicates 'W'.

# GUI configuration File
  This file is created and updated exclusively by the GUI program. It is used to save and restore various parameters, panel settings, and screen positions during the course of the GUI operations. The file is stored in the User's HOME directory ('~') with the name radioctl.vars.

Each record identifies a variable in RadioCtl and what the value should be when the program is started. The variables are usually multi-keyed hashes. In general the record will be interpreted as a PERL assignment statement.

The user should NOT modify the contents of this file, as it could cause the RadioCtl program to fail. However, the file CAN be erased before starting RadioCtl if the user desires all settings for the program to revert to the original values.