        RADIO CONTROL PROGRAM FOR LINUX

By Lydia & Richard Rosa

Last update: 11/26/23

Copyright 1995-2023 by Lydia & Richard Rosa

# What's New In This Release
Version 0.04.106 09/05/23 - Beta Release – Lots of Bug Fixes
Version 0.04.107 09/14/23 - More Bug Fixes. General Cleanup
Version 0.04.108 09/26/23 - More Bug Fixes.
Version 0.04.109 10/18/23 - Still MORE Bug Fixes
Version 0.04.110 10/29/23 – Added ICOM IC-7300 support.
Version 0.04.111 10/30/23 - Added installation script
Version 0.04.112 11/15/23 - GUI bug fixes
Version 0.04.113	11/26/23 - Changes for split/offset

# License
  This program is distributed as charity-ware. There is no cost to use this software. You may freely distribute this application as long as you do NOT collect a payment for such distribution, and that the LICENSE file is included with that distribution.

 If you find this program useful, please donate what you think it is worth to your local food bank or charity.

# DISCLAIMERS
ICOM is a trademark of ICOM incorporated.
KENWOOD is a trademark of Kenwood Corporation.
AOR is a trademark of AOR
BEARCAT is a trademark of Uniden Corporation.

IMPORTANT WARNING: All software, including RadioCtl, contains undiscovered errors (also called 'bugs'). Although the chances are slight, these errors COULD result in loss of data or loss of functionality of the radio being connected. When you use RadioCtl, you assume all risks of this possibility. The authors can take no responsibility for any damages that may occur to your radio or computer due to the operation of this program.

Due to the charitable nature of this program, bug fixes and suggestions will be acted upon at the author's convenience.

Please e-mail all problem reports and suggestions to the authors at richardrosa@yahoo.com

The latest versions of RadioCtl can be downloaded from: https://github.com/richardrosa-rc/RadioCtl

Donations of radios for testing or inclusion in this program will be graciously accepted. Please contact the authors by e-mail if you want to make such a donation.

A big THANK YOU! goes out to David for helping to test this program.

Enjoy!

Lydia & Richard Rosa

# REQUIREMENTS

In order to run this program you will need the following:
- A Computer running a Linux distribution (Ubuntu/Mint/SUSE/etc)
- about 10mb of free disk space (for the program and document).
- about 500mb of free memory (more is always better).
- An interface cable to connect your computer to the radio.
- Pulse Audio installed (for recording).
- One (or more) of the following models of radio:
  - ICOM R-7000
  - ICOM IC-703
  - ICOM IC-R30
  - ICOM IC-7300
  - Other ICOM radios*
  - Bearcat BC895xlt*
  - Kenwood TH-F6A
  - Uniden BCD325P2
  - Uniden SDS100
  - Uniden SDS200
  - AOR AR8000

*Although not tested, this program MAY work with other models of this manufacturer equipped with an RS-232 or USB port.

# INTRODUCTION

The Radio Remote Control Program (RadioCtl) for Linux will allow you to control and/or program selected radios from a computer using serial (RS232) or USB ports with Linux. This program expands the capabilities of your radio, and provides an easy way to update or copy the data stored in that radio.

This is the fourth generation of this application. Prior versions were written to run under DOS, OS/2 and Windows. These prior versions are no longer being supported.
Note that this version of the program is EXCLUSIVELY designed for Linux distributions. Although it is written in the PERL programming language, it will most likely NOT function in a Microsoft Windows Environment.

### Defining Some Terms
There are various terms and descriptions used throughout this manual. Although RadioCtl is fairly easy to use, it helps to have a clear picture of what the program is doing and how it is doing it. Various terms are used throughout this document to explain the program operation.

VFO	Stands for Variable Frequency Oscillator. This is the settings for one frequency, modulation, and other parameters that tune the radio and set selected functions. Both the RadioCtl program and the radio being run have VFOs. Some radios may have two VFOs. However, RadioCtl will select only one of these to be the active VFO. RadioCtl's VFO is where parameters are sent to or received from the Radio's active VFO.
MEMORY	Memory is where multiple VFO settings are saved for future usage by the VFO. Both RadioCtl and most radios have memories. In some of the supported radios, the memory consists of information on a Secure Digital ('SD') Memory Card. The limit on RadioCtl's memory is pretty much limited by the amount of memory in your computer. The number of memories in the radio varies from model to model. RadioCtl memories may NOT always reflect the contents of the radio's memories. RadioCtl memories are also referred to as RECORDs in this document.
CHANNEL	Channel in this document refers to the radio's memory number. A channel number MAY be stored in a RadioCtl record.
GROUP	A group is a is a collection of records. Groups are used to collect records that are for similar services. Some radios (such as the BCD325P2) also have the ability to store groups in the Radio's memory.
SYSTEM	Like GROUP, system identifies a collection of Groups and Records that are part of a particular system. Some radios (such as the BCD325P2) also have the ability to store systems.
PROTOCOL	A method of communication with a particular radio. Each radio type has a unique method of transferring information between the radio and the computer. The method used by RadioCtl can be selected by the user, or based the make and model of the radio being controlled.
PROGRAMMING	All radios have the ability to save certain information for later use in their memories. This saving is referred to by RadioCtl as programming. Most of the radios supported by RadioCtl can be programmed.
CONTROL	Radios supported by RadioCtl can also be controlled. This means that the radio can be used to scan and search using the RadioCtl facilities. Some radios have limited control ability, so some of the control features in RadioCtl may not be available.
STATE	The current operation that RadioCtl is performing is referred to as a state. For example, the GUI program will start in the MANUAL state.
DATABASE	A collection of information used by RadioCtl. There are several databases available in RadioCtl including the Frequency Database and the Search Bank database. Each database is displayed on a separate panel in the GUI.
RECORD	A single row in one of the RadioCtl database panels, or a row in a RadioCtl data file.
FREQUENCY	The location in the radio spectrum where a transmission occurs.
MODULATION	The transmission method that a radio signal uses to encode audio (or other information)
TONE	An analog or digital addition to the audio in a transmission that is used to allow multiple agencies to share a single frequency.
SERVICE	The name of the agency or organization that utilizes a Frequency and Modulation in the radio spectrum.
CONVENTIONAL	A system where a single frequency is assigned to one agency or service.
TRUNKED	A system where a range of frequencies are assigned to a single system, to be shared by more than one service.
SITE	For a TRUNKED system, the frequencies for a single location. A TRUNKED system can have more than one site.
SIMPLEX	This is a system where all users of a service utilize the same frequency.
DUPLEX	Many radios that can transmit allow for different reception frequencies from the transmission frequencies. This difference allows for utilization of a 'repeater' designed to increase the coverage of a low-wattage radio. DUPLEX can also be used so that a strong BASE transmitter does not 'drown out' weaker MOBILE units. / Some of the radios supported by RadioCtl can monitor BOTH input and output frequencies of these repeaters. A couple of the supported radios can also transmit (on Amateur Radio Frequencies) to these repeaters. / NOTE: An FCC license is REQUIRED for transmission!
OFFSET	For DUPLEX systems, this is a frequency that is added or subtracted from the receive frequency to get the input frequency to a repeater.
SPLIT	For DUPLEX systems, this is a set of specific frequencies for Input and Output of a repeater, instead of adding or subtracting an OFFSET,

# Installation
To install the program, download the program into a directory that you have write access to. If the program was received as a .zip or .gz file, uncompress it into that directory.
 Open a terminal and type the following commands:

      cd /directory_where_the_files_are
      perl install.pl

If you wish a desktop ICON to be created:
     cp radioctl.desktop ~/Desktop/

The GUI program can be started from the application launcher.

 You can also start from a terminal using the commands:

    ./radioctl ### for the GUI
    ./radiowrite {cmd} ### for the command line operations

# Program Overview
RadioCtl provides the user with a flexible way of controlling and programming a radio. It also provides a uniform interface for different types of radios.

There are two pieces to this program. The first is a Graphical User Interface (GUI) that is designed to expand the functionality of your radio. The GUI makes it easy to locate and monitor frequencies that are in use in your location.
The second program is a command-line tool used to save and recall the memory channels in your radio.

NOTE: Due to the limitations of certain Desktop Environments, the GUI program may need to be started from a terminal, rather than the Desktop File Manager.

Radio control information is sent to and received from the radio by way of a serial port. This serial port can be an RS232 type, or USB type. The program provides for selection of different radios, each with a unique set of operation characteristics. The actual commands to the radio are defined by a protocol setting. The program supports protocols for a number of different radio makes and models.. A 'simulated' radio ('Local' protocol) is built-in to RadioCtl so that the features can be explored without a radio being connected.

The hardware to connect the computer to the radio varies based on the radio. For ICOM radios, a CI-V to USB port cable is available. For Kenwood, an adapter for USB is also available. The AOR-8000 requires a flat wire cable and an interface box to RS232 from OptoElectronics. The Bearcat BC-895xlt utilizes a 5 pin RS232 connection. All other radios provide a standard USB cable connection.

## Supported Radios

This is a list of all radios currently supported by this program. Due to the limitations of the radio, some functions of RadioCtl may not be available. Note that any data stored in the radio's memory MUST be done using the command line program radiowrite. The GUI is only able to read the contents of the radio's memory, and ONLY for conventional (non-trunked) frequencies.

radio	Limits
ICOM R-7000	This radio lacks the ability to detect squelch break or signal presence. Because of this, logging and recording operations are not possible. No channel text ('service') can be stored in the radio's memory. No split or duplex settings can be set. / The 'Radio Scan' operation is not functional with this radio. / Tone squelch, attenuation and preamp settings are not functional with this model.
ICOM IC-R30	The current command set for this radio does not provide the ability to store into the radio's memory from the program. The radiowrite program provides a command to export RadioCtl data to the format used by the SD card. This is the ONLY way to update the radio's memory. / The radio does NOT support split frequency operation. However, duplex setting IS possible using the SD card ONLY. / Although there are three levels of Attenuation, RadioCtl will always set ATT1 when attenuation is selected. / The radio also has a 10 level RF amplifier. The individual values of this amplifier can be set in each memory channel using the SD Card. The GUI will select the RF level based on the ‘preamp’ and ‘atten’ settings: / preamp atten RFG / Off Off RFG5 / Off On RFG1 / On Off RFG MAX / On On Not allowed in RadioCtl / The radio has 100 groups (0-99). Each group has 100 Channels (0-99). Radioctl will map these to channels 0 – 9999. / Ex: RadioCtl channel 2123 maps as Group 21, channel 23 in the radio. / Reading group names is NOT possible. Group names CAN be set using the SD Card. / Digital audio modes supported by the radio can be set in memory using the SD Card. The GUI does not support any of these digital modulations. CTCSS and DCS squelch settings are also recognized and supported by the GUI. / The Linux driver for the Radio's chipset requires some additional system commands to allow the radio to be recognized by the Linux system. These commands will need SUDO access: / sudo rmmod cdc-acm / sudo modprobe cdc-acm / sudo echo 0c26 002b 2 076d 0006>/sys/bus/usb/drivers/cdc_acm/new_id
ICOM IC-703	This is an Amateur Radio Transmitter that can also be used as a scanner. / The maximum frequency that can be utilized is 60mhz. Split frequency settings (but NOT duplex) are supported. / CTCSS squelch settings are supported, as are attenuation and preamp.
ICOM IC-705	This is an Amateur Radio Transmitter that can also be used as a scanner. The maximum frequency that can be utilized is 470mhz. There is also a gap in coverage between 200 MHz and 400 MHz. / Both Split and Duplex frequencies can be set in memory. SD-Card data can be generated using the radiowrite program. / Both CTCSS and DCS squelch operations are supported. The GUI does not support D-Star modulation. However, the values CAN be set using the command line routine. / Attenuation is ONLY functional on the HF (Below 30mhz) and 50mhz bands. / The radio has 100 groups (0-99). Each group has 100 Channels (0-99). Radioctl will map these to channels 0 – 9999. / Ex: RadioCtl channel 1103 maps as Group 11, channel 3 in the radio. / Reading group names is NOT possible. Group names CAN be set using the SD Card. / Although the 'Radio Scan' operation works, only the Frequency and Modulation settings can be logged.
ICOM IC-R8600	Although similar in functionality the ICOM IC-R30, memory values CAN be stored directly. Duplex is supported, but not split. / The radio has 100 groups (0-99). Each group has 100 Channels (0-99). Radioctl will map these to channels 0 – 9999. / Ex: RadioCtl channel 0123 maps as Group 1, channel 23 in the radio. / Reading group names is NOT possible. Group names CAN be set using the SD Card. / NOTE: none of the code in place has been executed against a real radio, so it MAY not be functional.
Uniden BCD325P2	This radio uses dynamic memory allocation. As such, there are no individual channel numbers, so the GUI 'Scan By Radio's Channel' operation cannot be used. / Trunking is generally not supported in the GUI program. However, trunked system scanning IS available using the 'Radio Scan' operation. / The GUI operation 'Load From Radio' is limited to Conventional systems only. / The Load of the radio's memory is limited to conventional systems for the GUI. / The radio's memory structure is similar to RadioCtl's data structures. / Split and Duplex channels are NOT supported.
Kenwood TH-F6A	The communications interface for this radio disables the internal speaker. Additional hardware will be needed for listening to or recording audio. / The GUI 'Radio Scan' operation is not supported for this radio. / Split frequencies can be save or read from the radio's memory. / Duplex is NOT supported. RadioCtl records that indicate Duplex will be converted to SPLIT frequencies before being stored.
Bearcat BC-895xlt	Trunking settings are not supported by the GUI or command line. / No channel text ('service') can be stored in this radio. / Split and Duplex channels are NOT supported. / CTCSS and DCS tone squelch are ONLY available when stored in the Radio’s memory. Tone squelch CANNOT be processed from the RadioCtl GUI.
Uniden SDS100/SDS200	These radios utilize micro-SD cards for the radio's memory. Because of this, storing data directly into the radio is not provided by the program. However, Favorites lists destined for the SD card can be created/updated from RadioCtl data files using the radiowrite command line program. / Like the BCD325P2, there are no individual channel numbers, so the 'Scan By Radio's Channel' operation is not functional in the GUI.

# GUI interface
  The GUI program is radioctl. The program can be started from a terminal by executing ./radioctl after changing to the directory where the program has been placed. The program may also be started from the Linux Desktop IF the file is marked as executable, and the File Manager (such as Dolphin) allows for shared library applications to be run.
NOTE: Nautilus (the default File Manager for Ubuntu) currently will NOT allow for this application to be run by selecting the file. For Ubuntu, an application launcher will need to be built if this file is to be run from the desktop.

When the application is started it will present the user with a graphical interface to control your radio. Using this interface, you can
- Set frequency and modulation on the radio.
- Load data from the radio's memory.
- Record the radio's audio when there is a signal.
- Search a range of frequencies for activity.
- Log activity for frequencies stored in the radio.
- Scan and log activity on trunked systems (using the Radio's memory).
- Perform a number of radio functions from a common interface.

The GUI program presents multiple panels for the various databases and controls. Initially, all windows and panels on those windows are displayed. The 'view' menu allows you to disable (or enable) those panels and windows. The program will save your preferences when the program ends, and restore those settings when the program is restarted.

The MAIN window (which is always displayed) contains controls for selecting an operation (Scan, Search, etc), viewing the program's status, setting options and setting the VFO of the radio or program. Other windows display the contents of the RadioCtl databases (Frequency, System, Group, Search, etc).

## MAIN Panel Operation
The MAIN window is used to control all operations. In order to perform ANY operation, a radio needs to be connected. RadioCtl provides a simulated radio ('local') that is automatically connected when the program starts. This simulation allows you to try out the various functions of the program without the need for a radio to actually be connected.

To connect your radio, locate it in the 'Radio Selection' panel, 'Radio' drop-down control, then press the 'Status' button to attempt connection. If the radio is successfully connected, the button will display 'Radio Is Connected' in green. Normally, the program can automatically figure out the baudrate and serial port to use. However, if the program cannot determine this automatically, uncheck the 'autobaud' control and set the 'port' and 'baudrate' as needed. If a radio is plugged in to a Serial or USB after the program is started, the 'rescan' button will reload the serial/USB ports available.

The radio selection is determined by the contents of the file radioctl.conf in your HOME directory. If you need to update this, the file can be reloaded by selecting the File → Read Radio Definition menu item.

The 'Status' panel displays the current system, group and frequency numbers, as well as current delay and resume values. The current count of database records is also displayed.

The Signal Meter will display any signal that is detected from the radio. For the Local radio, clicking on a signal meter button will turn 'on' the local radio's signal. The 'Off' button will turn off the local radio's signal. During a Scan or Search operation, the 'Off' button will effectively resume the search or scan operation if a signal is present. The 'squelch' control can be used to limit the strength of the signal that the program detects.
NOTE: Not all of the supported radios have the ability to report the signal strength. For those radios, the signal level (when a squelch break is detected) will always be reported as 9.

The 'Speed Limit' control is used during search or scan operations to slow the rate of channel or frequency change. This may be needed to give the radio time to settle between changes.

The VFO panel displays RadioCtl's VFO status If the connected radio’s status changes, the changes are normally reflected in the RadioCtl VFO displays.
Channel number, Step and Frequency values can be changed using the UP/Down buttons next to the display, entering a value in the input box under the display, or clicking on a single digit. Changes to these controls MAY result in a change in the Radio's VFO, depending on the current operation.

If enabled, there is also a control for selecting the Radio’s channel. When changed, the connected Radio’ selected channel number will change, and the contents of that channel will be reflected in RadioCtl’s displays.

Operation Options allow for changing the way that certain operations perform. Each option has an 'enable' check-box that turns that option on. Some options also have a value that the user can change. How each option works is detailed in the next section (operations).

The database windows allow for displaying and changing the RadioCtl databases. Each line in the window (called a 'record') represents some set of parameters. Each element of this set (referred to as a 'field') represents a single parameter (frequency, modulation, etc). Most of these parameters are controls that can be changed, however, some fields are not user changeable. Most notably, the INDEX field uniquely identifies each record. All fields can be selected for viewing (or hiding) using the View menu item. Records can be added by loading a file (using FILE->Open menu item), as a function of a particular operation, or using the Edit -> Add A Record menu item.

Most operations allow for recording activity to a .wav file. This file will be updated whenever a signal is detected by the program. The filename of the recording will be the frequency of the signal with a '.wav' file extension. If a recording file already exists, the new recording will be appended to the old one. This feature allows you to extract out activity on one or more frequencies over the course of time, excluding periods of inactivity.
The directory where recordings are kept is defined in radioctl.conf. If not specified, defaults to ~/recording (in user's home directory).
In order to make use of this feature, your radio will need the audio connected to the computer. A connection to the Radio's Headphone or external speaker jack should be made to the input connection of your computer's sound card.
The input source of the recorded file is determined by the settings of the sound system installed in Linux. For most Linux distributions, this is Pulse Audio, or Jack. These settings may need to be modified to direct the input from the sound card to the RadioCtl recording function. For PulseAudio, the selection is done through the pavucontrol tool.

## Controls
There are a number of different types of controls for changing memory channel information, current radio settings ('VFO') and operation parameters.

### Frequency Controls
There are two sets of frequency controls: Frequency and Step. Each control has a number of digits, a pair of up/down keys and an entry field. If the control is enabled (some operations MAY disable the control), the value in the control can be set by ANY of the following actions:

- Entering a new value in the input box below the control.
- Pressing the UP or DOWN button next to the control.
- Hovering the mouse pointer over a digit and pressing a mouse button or moving the mouse wheel.
When using the input box, any number between 1 and 9999.9999999 can be entered (0 is NOT allowed). If a decimal point is specified, the value is assumed to be in MHz. Otherwise the value is assumed to be in Hz.

If using the mouse on a digit: Right click will increase the digit by 1, left mouse will decrease the digit by 1. The mouse wheel will ‘scroll’ the digit up or down depending on the direction of the wheel.

For the frequency control, the display may (or may not) reflect the actual value in the connected radio’s VFO. Pressing the up or down button will add or subtract the current value in the step control, and possibly send that value to the radio. If the radio accepts that frequency, the display will be updated. Otherwise, the display may remain unchanged.

The step control is never sent to the radio. It is used exclusively by RadioCtl for increasing or decreasing the Frequency value.

### Modulation Controls
   Modulation is selected using drop-down boxes. As with frequencies, not all modulations are supported by all radios. When sending modulations to the radio, the program may translate the value into something that the radio understands. Likewise, the radio may also ignore or change modulations it does not understand.
Note that the GUI does NOT support digital modulations (DMR/P25/D-Star/etc)

Modulation	Description
FMw	Frequency Modulation Wide. This is the modulation used by broadcast FM stations in the 88-108mhz range (75khz deviation). / If the radio provides support for frequencies in the FM broadcast band, this modulation will be available. / If the radio does NOT support FMw, the modulation will be changed to FMn
FMm	This is the modulation used by analog TV stations for the sound carrier (25khz deviation). Because analog TV is pretty much obsolete, not many radios support this. / If the radio does NOT support FMm, the modulation will be changed to FMn
FMn	This modulation is used by most of the frequencies in the VHF & UHF public service bands (5khz deviation). All of the radios supported by RadioCtl recognize this modulation.
FMun	Ultra-Narrow Frequency Modulation (2.5khz deviation). For now, only the Uniden radios support this. For all other radios, FMn will be set.
AM	Amplitude Modulation. Mostly used below 30mhz & for the VHF Air band (108-136mhz). This modulation is recognized by all of the RadioCtl supported radios. / For radios with a bandwidth/filter selection, this will select a WIDE filter.
LSB	Lower Side-band. Generally only used on frequencies below 30mhz. / Only supported on radios that provide a full range of support for short-wave frequencies (20khz to 30mhz). / For radios that do not support this modulation, RadioCtl will change the modulation to 'AM'
USB	Upper Side-band. Generally only used on frequencies below 30mhz. / Only supported on radios that provide a full range of support for short-wave frequencies (20khz to 30mhz). / For radios that do not support this modulation, RadioCtl will change the modulation to 'AM'
CW	'Continuous Wave'. Used for Morse Code detection. Generally only used on frequencies below 30mhz. Only supported on radios that provide a full range of support for short-wave frequencies (20khz to 30mhz). / For radios that do not support this modulation, RadioCtl will change the modulation to 'AM'
CW-R	Continuous Wave Reverse'. Used for Morse Code detection. Generally only used on frequencies below 30mhz. Only supported on radios that provide a full range of support for short-wave frequencies (20khz to 30mhz). / For radios that do not support this modulation, RadioCtl will change the modulation to 'AM'

### Channel & Index Controls
A channel represents a memory location in the radio. An index is the record number in the 'frequency' database.

Each control has a number of digits, a pair of up/down keys and an entry field. If the control is enabled (some operations MAY disable the control), the value in the control can be set by ANY of the following actions:

- Entering a new value in the input box below the control.
- Pressing the UP or DOWN button next to the control.
- Hovering the mouse pointer over a digit and pressing a mouse button or moving the mouse wheel.

Index values can be any number between 1 and 99999 (0 is NOT allowed for an index). Channel numbers can be 0 to 9999. Decimal points (and any other non-numeric input) are NOT allowed.

Changing the index control will transfer the contents of the selected Frequency database record to the VFO display. If there is a connected radio, this will also transfer those values to the radio’s VFO. If there is no defined frequency record for that index, all values (including the index) will remain unchanged.

Changing the channel control will instruct the connected radio to select that channel, and set the contents of that channel back to the program’s displays.
NOTE: For Uniden dynamic radios, changing the channel control will NOT result in any changes to the radio. These radios do NOT have individual channel numbers.

### Extra Controls
    These settings may or may not be supported by the connected radio. These controls are selected using drop-down lists in both the main panel (‘VFO’) and the frequency database panel.

Control	Description
Att/preamp	Turns on a setting in the radio that reduces or increases the signal level.
CTCSS	Prevents the radio from breaking squelch unless the specific tone is present
DCS	Prevents the radio from breaking squelch unless the specific code is present

NOTE: Even if the radio supports it, CTCSS and DCS squelch is ONLY functional if the modulation is FM (FMn/FMun/FMm).
### Operation Options
These are selections that modify what happens when a particular operation is happening. The function of each of these is dependent upon the current operation being processed.

#### Signal Delay/Resume
  This control determines the action AFTER a signal is detected. Both the value and the checkbox must BOTH be set in order for this option to be active.

If the value is a positive number, and the checkbox is checked, the program will delay for the number of seconds specified AFTER a signal was present, but went away before proceeding to the next channel or frequency.

If the value is a negative number, the checkbox is checked, and a signal is present, the program will continue to the next channel or frequency after the number of seconds specified.

If the value is 0, or the checkbox is unchecked, the value in this control is ignored.

If the value is 0, but the checkbox is checked, the delay or resume value and action will be taken from the currently selected frequency database record.

This control is NOT used in Manual or Radio Scan operations.

#### Starting/Ending Channel/Record
 Certain operations allow specification of a starting and or ending value. The values can be for a Radio Channel number, or for a RadioCtl Frequency database record. For RadioCtl records, the value must be 1 or greater. For radio channels, the value CAN be 0 if this is a valid channel number in the radio.

A start value can be used without a stop value. Likewise a stop value can be used without a start value. The program will use default values if not selected.

The start or stop value will ONLY be used if the corresponding checkbox is selected.

#### Use System/Group Records

Normally, scan operations will only select value frequency database records. However, if either (or both) of these options is selected, the System and/or Group records that each frequency record references must also be marked as valid to be used in that scan.

#### Update Database In Manual
When in manual state, any signal that is received from the radio is normally NOT logged to the frequency database. This option will force logging even when in manual state.

#### Record Audio when Signal
 If selected, any available audio will be recorded to a .wav file. The input for this recording will be set by whatever is selected by the Linux sound system (PulseAudio/Jack/etc). The location of this file is determined by the configuration file in your HOME directory. The filename will be the frequency (in MHz) indicated by the program’s VFO display.

This option is functional in ALL states.

#### Log Events to this file
If the checkbox is set, any signal detection is logged to the file specified. The directory of the file is determined by the configuration file in your HOME directory.

This option is ignored in manual state UNLESS the ‘Update Database In Manual’ option is also selected.

## Operations
Each operation is selected with one of the Operation buttons. Some operations have requirements that must be met before they can proceed. Others may not be available for the particular radio. Operation Options may change the way that a particular operation works. Selecting an operation places the program in that 'state' until the operation is terminated, or completed.

### Manual
 This is the default state of the program. When the program starts, this will always be the state that it starts in. When another operation terminates, this will usually be the state that it returns to.
In Manual state, the following happens:
- Any change to the Frequency or Modulation of the radio is reflected in the program's VFO settings and displays.
- If there is a squelch break, the Signal Meter will indicate the signal strength (value will be 9 if the radio does not allow for reading a signal strength)

The following Operation Options affect Manual state when selected:
option	function
Update database in Manual	A database record will be added or updated when a signal appears. / This record will contain the frequency, modulation, time of signal on, duration of the signal on, and the signal strength. In addition, a count of the number of times this frequency was active is also updated.
Record audio when signal	An audio recording will be made when a signal appears.
Log events to this file	A log entry in the file specified will be made after each squelch break. / This ONLY works in manual mode if the 'Update database in Manual' option is also selected.

The following VFO controls are functional during Manual State:
control	Function
Signal Meter Off	If using the Local radio, this will turn off the signal. For all other radios, this button does nothing in manual state.
Signal Meter Segment	If using the Local radio, pressing one of these segments will turn on the signal at the selected level. For all other radios, pressing one of these segments does nothing in manual state.
Frequency	Any change in frequency will be sent to the radio, along with the current values of Modulation, Att/Preamp, ctcss & dcs. / The resulting values that the radio responded with will be updated in the VFO displays. Note that these values MIGHT be different than what was attempted to be set.
Index	Changes to this control will cause the contents of the RadioCtl frequency record number to be set in the program’s VFO. If there is a radio connected, the settings will also be sent to that radio’s VFO. Any differences in the Radio’s values will be reflected in the program’s displays. / Note that the selected database index MUST already be present, or the changes to this control will be ignored.
Channel	This control will change the memory channel of the connected radio. The values in that memory channel will be reflected in the program’s displays.
Step	The value set will be used when the Up/Down buttons of the Frequency control are pressed. The Step value is NEVER sent to the radio.
Modulation	If there is a radio connected, any change in this control will result in the new modulation selected being sent to the radio. In addition, the current values of / Frequency, Att/Preamp, ctcss & dcs will also be sent. / The resulting values that the radio responded with will be updated in the VFO displays. Note that these values MIGHT be different than what was attempted to be set.
Extra Controls	If there is a radio connected, any change in these controls will result in the new value being sent to the radio, along with the current values of Frequency & modulation. / The resulting values that the radio responded with will be updated in the VFO displays. Note that these values MIGHT be different than what was attempted to be set. This will be especially true if the radio does NOT support one or more of these extra controls.

### Scan by Database Frequency
This operation will loop through all Frequency database records. If a frequency record has the 'valid' flag reset, then that record will be ignored. The frequency of the database record must be within the range of the radio. Depending on options selected, other criteria for selection may also need to be met.

Once a valid record has been located, the frequency and modulation specified in that record is sent to the VFO of radio. If the radio supports it, tone, attention and preamp information may also be set. The values that are actually set in the radio will be reflected in the RadioCtl VFO. The program will then look for a signal from the radio. If one is detected, the scan will pause until the signal goes away. When the signal terminates, the record that was selected is updated with the signal level, time of first squelch break, duration of signal and count of squelch breaks. The time that the radio waits for another signal from the same VFO settings is determined by the SPEED control as well as any enabled resume value.

The speed of each record process is also dependent on the radio. All of the radios supported have a certain amount of latency when setting the frequency. This latency defines how long after the radio is tuned to a particular frequency before the radio can detect a signal. Delays have been added to RadioCtl to allow for this latency.

Scan by Database Frequency will terminate if there are less than two records in the frequency database that meet the selection criteria.

This operation only increments record numbers. The up/down controls do NOT affect the scan direction.

Table 1: Options affecting Scan By Database Frequency/Scan By Database Channel
option	function
Resume/Delay	If selected, Resume or delay will be processed. If the value in the option is 0, then the resume or delay function is determined by the currently selected frequency database record.
Starting/Ending	If selected, the Database frequency Records selected must be greater than or equal to the starting record, and less than or equal to the ending record. / The record numbers specified MUST be greater than 0 (record 0 is NOT a valid radioctl index). / The default value for Start is 1, and the Ending value is the last frequency database index.
Use System records.	If selected, any system records are selected in sequence and frequency records that reference this system number are used. Only system records marked as valid are used.
Use Group records.	If selected, any group records are selected in sequence and frequency records that reference this group number are used. Only group records marked as valid are used. / NOTE: If system records are also used, both group AND system numbers must match for the frequency record to be used.
Record audio when signal	An audio recording will be made when a signal appears.
Log events to this file	A log entry in the file specified will be made after each squelch break

Table 2: Controls for Scan by Database Frequency
Control	Function
Frequency Up/Down/Digit/Entry	If a signal is present, the program will turn off the signal and move to the next valid frequency database record. If a frequency is entered, it is ignored.
Signal Meter Off	If there is a signal, turn it off and move to the next valid frequency database record.
Modulation	The radio will be changed to the selected modulation. / This MAY cause the signal to change or turn off.
Extra Controls	Any changed value will be sent to the radio. The radio may or may not accept these values. If it does, the change MAY cause the signal to change or turn off.
Squelch	If the bar is set to anything other than 0, signal levels that are BELOW the value set will not cause the scan to stop.
Speed Limit	The rate of scan can be slowed using this control. This control adds some delay between setting each channel or frequency into the radio. During this delay, the radio is checked for a signal. / This control is used for radios that need more time to stabilize when a frequency is set.
Database Record Valid	If the valid flag is turned off for an active frequency database record, the signal will be turned off and the scan will move to the next valid record. / If Use System Records or Use Group Records is selected, Turning off the valid flag on the active System or Group record will also terminate the signal.

### Scan by Radio's Channel
  The program will loop through all Frequency Database records. A database record will be selected if the following conditions are met:

- The ‘valid’ field must be checked.
- A numeric channel number must be entered in the ‘channel’ field.
- The channel number is within the memory range of the connected radio.
Once a record meeting all the criteria has been found, the radio’s memory channel indicated in that record will be selected. All other fields in that record are NOT used.

After the channel has been selected, a check will be made for a signal on that channel. If a signal is found, the Frequency, Modulation and other information will be updated in the RadioCtl record that was selected.
The program will move to the next database record once the signal has gone away.
The time that the radio waits for another signal from the same VFO settings is determined by the SPEED control as well as any enabled resume value.
If the user changes the ‘valid’ checkbox on the Database record while a signal is present, the program will ‘terminate’ the signal and proceed to the next Database record.

The speed of each record process is also dependent on the radio. All of the radios supported have a certain amount of latency when setting the frequency. This latency defines how long after the radio is tuned to a particular frequency before the radio can detect a signal. Delays have been added to RadioCtl to allow for this latency.

Note: This operation is not available for Uniden Dynamic Radios, as there are no channel numbers.

Table 3: Options affecting Scan By Radio's Channel
option	function
Resume/Delay	If selected, Resume or delay will be processed. If the value in the option is 0, then the resume or delay function is determined by the currently selected frequency database record.
Starting/Ending	If selected, the channel referenced in each Frequency Record must be between the starting and ending numbers specified..
Record audio when signal	An audio recording will be made when a signal appears.
Log events to this file	A log entry in the file specified will be made after each squelch break

The following controls can be used during a Scan By Radio's Channel operation.

Table 4: Controls for Scan By Radio's Channel
Control	Function
Index/Channel Up/Down	If a signal is present, the program will turn off the signal and continue processing with the next valid frequency database record.
Frequency Up/Down	If a signal is present, the program will turn off the signal and continue processing with the next valid frequency database record.
Signal Meter Off	If there is a signal, turn it off and move to the next (or previous) channel.
Squelch	If the bar is set to anything other than 0, signal levels that are BELOW the value set will not cause the scan to stop
Speed Limit	The rate of scan can be slowed using this control. This control adds some delay between setting each channel or frequency into the radio. During this delay, the radio is checked for a signal. / This control is used for radios that need more time to stabilize when a frequency is set.
Database Record Valid	If the valid flag is turned off for an active frequency database record, the signal will be turned off and the scan will move to the next valid record. / If Use System Records or Use Group Records is selected, Turning off the valid flag on the active System or Group record will also terminate the signal.

### Radio Scan
  This operation lets the radio do the scanning, while the program monitors squelch breaks. Using this function, it is possible for the program to scan trunked systems.
When selected, the radio is placed in a SCAN state. Some radios may require the user to press a button to start the scan. RadioCtl will then start monitoring the radio's squelch.

When a signal is detected from the radio the following actions are taken:
- The frequency. modulation, and other information is logged to the Frequency database. If the radio is scanning a trunked system, the Trunked Group ID (TGID) and possibly the description of that TGID will be logged.
- The first database record with the same frequency and tone squelch setting will be updated. If this is a trunked system, the TGID will be compared
- If no existing database record is found, a new one will be created with the current values reported by the radio.
- If the VALID flag is turned off for an existing database records. no information will be updated, and any audio recording will be suppressed. This is provided as the program CANNOT force the radio to skip a channel during Radio Scan.

A number of radios (such as the ICOM IC-705) do not provide a way to determine what channel is active and the 'service' data associated with that channel. For these radios, RadioCtl will set the service string to 'Found mm/dd/yy mm:ss Signal:x', and assign to the group 'Autolog Group'.

Radio Scan bypasses the latency issue for Frequency Scan and Channel Scan operations. All radios will scan SIGNIFICANTLY faster using the radio’s internal software instead of the computer interface. The SPEED control is not functional during the Radio Scan operation.

NOTE: Not all radios can perform a Radio Scan operation.

Table 5: Options affecting Radio Scan
option	function
Record audio when signal	An audio recording will be made when a signal appears.
Log events to this file	A log entry in the file specified will be made after each squelch break

### Frequency Search
  Starting with the frequency displayed in the VFO panel, the radio's VFO is set and a check is made for a signal. If no signal is found, the frequency is incremented by the 'step' value in the VFO panel, and the search continues. When the frequency exceeds the upper limit of the connected radio, the next frequency will be the lower limit of the radio. Pressing the 'up/down' controls will change the direction of this search.

The current frequency or step value can be changed at any time by using the Up/Down buttons, or entering the new value in the box under each display.

The 'Modulation' control will determine the modulation set in the radio. It can be changed at anytime during this operation. Note that not all of the supported radios allow for setting the modulation, and those that do may not support all of the modulations available to the program.

The ctcss, dcs, and atten controls are disabled during search operations. Search operations currently do not use tone decoding and attenuation settings.

When a signal is detected, the search will pause until the signal goes away. If there is a record in the frequency database with this frequency and modulation, it will be updated with signal level, duration of signal, and timestamp. If there is no matching record, a new one will be created. If there are multiple records with the same frequency and modulation, then the first one encountered (using the 'index' field) will be used.

When a new Frequency Database record is created during search, the Lookup Database will be searched for a matching frequency. If found, this record will be used for the 'service' field of the new Frequency Database record. Otherwise the service will be 'Found During Search'..

If an existing Frequency Database record has the 'valid' flag off, then that frequency will not be included in the search.

Delay and Resume controls on each Frequency Database record work the same way as they do on Scan operations. If the Operation Option is selected, the option is applied to all records. Otherwise, the option is only applied to the record with that option selected.

Table 6: Options affecting Frequency Search
option	function
Resume/Delay < 0 / and selected	Continue to the next frequency after the number of seconds specified in the value of this option when there is a signal.
Resume/Delay > 0 / and selected	Pause for the number of seconds specified in the value of this option when the signal goes off
Record audio when signal	An audio recording will be made when a signal appears.
Log events to this file	A log entry in the file specified will be made after each squelch break

### Frequency Bank Search
 This operation is similar to the Frequency Search except that the range of frequencies, the step value, and the modulation are determined by records in the Search Banks database.

Starting with the first Search Banks record marked as valid, the Frequency of the radio is set to the lower limit of that record. If allowed, the radio's modulation is also set based on the value in the selected record.
The program will step through each frequency in the range using the 'step' value in that record. When the last frequency in the range is reached, the program will select the next valid Search Banks record and search using that records settings. If there are NO valid search bank records, the operation will terminate. There MUST be a least on record marked as valid for Frequency Bank Search.
NOTE: Search direction changes using Up/Down controls only affect the Frequency increment or decrement. The selection of bank records is always low to high.

The frequency, step, modulation, ctcss, dcs, and atten controls on the VFO panel are not functional during Frequency Bank Search. The frequency, step and modulation values are determined exclusively by the settings in each Bank record. Search operations currently do not use tone decoding and attenuation settings.

Table 7: Options affecting Frequency Bank Search
option	function
Resume/Delay < 0 / and selected	Continue to the next frequency after the number of seconds specified in the value of this option when there is a signal.
Resume/Delay >0 / and selected	Pause for the number of seconds specified in the value of this option when the signal goes off
Record audio when signal	An audio recording will be made when a signal appears.
Log events to this file	A log entry in the file specified will be made after each squelch break

### Load From Radio
When selected, the databases will be loaded with data from the connected radio’s memory channels. For radios that support trunked systems, only information from non-trunked systems are loaded.

This operation CAN take a long time, depending on the radio and the number of channels with information. During this time, all controls will be disabled. However, a pop-up will be displayed with a ‘cancel’ button. This allows you to abort the operation before it completes.

The following options are used during the LOAD operation:

option	function
Starting Channel	Start loading from the Radio’s channel number indicated. / For this option to be used, the number MUST be > 0 and the checkbox for the option set. / This option is ignored for Dynamic radios (Uniden) as there are no channel numbers in these radios.
Ending Channel	Stop loading after the Radio’s channel number indicated. / For this option to be used, the number MUST be > 0 and the checkbox for the option set. / This option is ignored for Dynamic radios (Uniden) as there are no / channel numbers in these radios. / NOTE: If both Starting and Ending Channels are selected and the Starting channel is LARGER than the Ending Channel, The numbers will be reversed such that the LOWER number will always be the first channel and the HIGHER number will be the last.
LOAD uses existing System	By default, a new system will be created when the LOAD operation starts. If this option is selected, an existing number will be used. However, if there is NO existing system when LOAD starts, this option is ignored.
Clear Database Before Load	If selected, all RadioCtl data will be cleared before the LOAD operation starts
Don’t Skip Empty Channels	By default, radio memory channels that are not used are NOT loaded. If this option is selected, these channels will be added to the FREQUENCY database (with a ‘0’ frequency). / This option has no effect for dynamic (Uniden) radios, as empty channels are NEVER present.
Don’t Keep Duplicate Channels	If selected, channel numbers that are already in the RadioCtl database will NOT result in a new record being added.

## Database Panels
  The database panels will display records loaded from RadioCtl data files, an attached radio, or user entered. Database records can be 'linked' to records in other databases. 'Frequency' database records can be associated with a system and/or a group record. Group records can be associated with a System record.

# COMMAND LINE PROGRAM
A separate command line program is provided that allows for processing RadioCtl files, Storing values into radio memories, Reading values from radio memories, and updating SD cards.

To start the command line program issue the following command from a terminal:
    cd /directory_where_program_was_placed
    radiowrite cmd input1 input2 ... options
'cmd' is a specific command, and 'input' is a file specification or radio name. Any input specification that contains a blank MUST be surrounded by quotes (ex: "Input With Blank"). If the input is a file specification, the full path of the file MUST be included if the file does not reside in the current directory. Not all commands require an input, and not all commands can process multiple inputs, Options follow the Unix standard of '-' for single letter and '--' for word options.

Any files created by these commands will be placed in a directory chosen in the following order:

1. If the --dir option is specified on the command, output will be placed there.
2. If --radio option specified (or the radio name is part of the command), and ‘sdir’ is included in the configuration file for that radio, this will be the directory where files will be placed.
  If multiple --radio options specified, the first one ONLY will be used.
  Some commands may also search for ‘sdir’ in radios of a specific model even if the --radio option is not specified.
3. If there is a ‘tempdir’ option specified in the control file, it will be used.
If all of the above are blank/not set, then the output directory will be radioctl in the User’s HOME directory.

If the determined directory does not exist. the program will attempt to create it. If the selected directory CANNOT be created, the command will terminate.

Commands to generate SD-Card data will also create additional sub-directories in the selected directory. These sub-directories will mimic the structure of the Radio’s SD-Card.

## BLOCKS
Inputs: Name of radio. Must be either a Uniden BCD325P2 or a Uniden BCD396T model.

 BLOCKS command will generate a list of ALL defined ‘blocks’ for each system in the specified radio. The report will include the amount of memory used, and the address for each of the allocated blocks for each system.

The output filename will be radio_name-blocks.txt, where radio_name is the name given as the input.

The following options are defined for the BLOCKS operation:

option	description
--dir directory	Directory to place output into. Overrides the standard directory selection.
--notrunk	Don’t include TRUNKED systems
--raw	Include the raw output from the radio. Used primarily for debugging this program.

## CSV2ICOM
Inputs: One or more file specifications.

This command will convert one or more CSV files to .csv files for ICOM radios. The destination files are intended to be used in the SD card that the radios load systems from. Output files will be named: ICmodel-group-xx.csv and ICmodel-all.csv, where 'model' is the model of radio (R30/705/etc) and 'xx' is the group (00-99). The 'xx' files are intended to be used for loading one group. The 'all' files are for loading the entire radio's memory.
Warning: The IC-705 will erase the ENTIRE memory even if only one group is loaded.

 If the --radio option is not used, the directory selection will include the first ICOM model found in the configuration list.

  The directory structure created in this sub-directory will be:
        ../ICOM_SD_FILES{model}/Csv/Memory/Ch
where '{model}' is IC-R30, IC-705 or IC-R8600.

The files generated are intended to be transferred to an SD card that the ICOM radio can read. These files can then be used to program the various groups and frequencies in the radio. Because the ICOM IC-R30 does NOT have any direct commands for storing memory, this is the ONLY way that RadioCtl can be used to set memory channels in this radio.

Only IC-R30, IC-705 and IC-R8600 support SD cards

The following options are recognized for the CSV2ICOM command:

Table 8: Options for SCV2R30 command
option	description
--dir directory	Directory to place output into. Overrides any defaults for output directory.
--radio model	Radio to generate output for. The model MUST be ICR30, IC705 or R8600. / More than one --radio option can be specified. / If not given, the output for all of these radios will be generated.

## CSV2HPD
Inputs: One or more file specifications.

This command will convert one or more CSV files to .hpd files for Uniden SDS radios. The destination files are intended to be used in the SD card that the radio loads systems from. See the documentation file RadioCtl-Data Files.odt for the file and record format for the input.

Each SYSTEM record in the input file (or files) results in one ‘f_xxxxxx.hpd’ file in the output directory. (‘xxxxxx’ is a number from ‘000000’ to ‘999999’). The number used will will either be taken from the ‘hpd’ key in the SYSTEM record of the input file, or defined (in sequence) starting with ‘000000’.

All SYSTEM records MUST have a quick-key defined. If one is NOT defined, the output for that system will NOT be generated. The ‘Favorites’ quick-key for that system will be assigned to the same quick-key. If the SYSTEM record ‘valid’ key is TRUE, then the quick-key for the System & Favorites will be turned on. Otherwise the quick-key will be turned off. However, if the key ‘turnqk’ is specified in the SYSTEM record, the quick-key will be turned On or Off based on the value of this key.

All SITE records MUST have a quick-key defined. If one is NOT defined, output for that site will NOT be generated. If the SITE ‘valid’ key is true, the Department quick-key for that site will be turned on. Otherwise the quick-key will be turned off. However, if the key ‘turnqk’ or the key ‘turndqk’ is specified in the SITE record, the quick-key will be turned On or Off based on the value of this key.

All GROUP records SHOULD have a quick-key defined. If one is NOT defined, the group CANNOT be selected by the radio. If the GROUP ‘valid’ key is true, the Department quick-key for that site will be turned on. Otherwise the quick-key will be turned off. However, if the key ‘turnqk’ or the key ‘turndqk’ is specified in the GROUP record, the quick-key will be turned On or Off based on the value of this key.

NOTE: Quick-keys for SITE and GROUP definitions are both assigned to Department quick-keys. Care needs to be taken NOT to assign the same key for SITE and GROUP.

For directory selection, the command will also include any ‘sdir’ in the first Uniden ‘SDSx00’ radio defined in the configuration file.
Files created in the output directory will be placed in the sub-directory ../BCDx36HP/favorites_lists/
This mimics the structure of the SD Card for SDS100/SDS200 radios.

Before the routine starts, any ‘f-list.cfg’ file in the output directory will be read. This file contains quick-key settings for each ‘favorite’ file, along with the system quick-keys. Any existing record in this file for a generated .hpd file will be updated. If the ‘f-list.cfg’ file does not exist, a new one will be generated.

These files are designed to transfer directly to the ../favorites directory of the Radio's SD card when that card is mounted (internally or through the USB) on the computer.

Note that the SD100 & SD200 radios do NOT contain any internal memory. All settings and programming reside on the SD card. Because of this, the CSV2HPD command is the ONLY way that RadioCtl can create the various systems for the radio.

The following options are recognized for the CSV2HPD command:

Table 9: Options for CSV2SDS command
option	description
--dir directory	Directory to place output into. Overrides the directory selection.
--hpd n	Set the first unassigned index. 'n' must be a number between 0 and 999999. If the SYSTEM record does NOT contain an ‘hpd’ key, the output file name will be set based on this index. Indexes will be assigned incrementally. / If this option is not specified, SYSTEM records without specified hpd values will be assigned numbers starting with 0. / ex: --hpd 3 option results in an output file f_000003.hpd for the next SYSTEM without an ‘hpd’ setting.
--force	Force assignment of hpd numbers regardless of the ‘hpd’ key in the SYSTEM record. This will assign numbers incrementally to each system starting with the number specified with the --hpd option. If --hpd is not specified, then the first number will be 0.

## FETCH
Inputs: Name of radio to read

This command will extract information from all or part of the memories of the radio specified. The output will be a RadioCtl .csv file. The output file name will be radio_name.csv.

Depending on the radio and the options, this command can take as long as 2 or 3 minutes to complete.

The following options are recognized for the FETCH command:

option	description
--append	Append data to any existing file. The default is to replace any existing file.
--count n	Count of systems or channels to process. For Uniden radios, this will be the number of systems returned. For all other radios, it will be the number of channels.
--dir directory	Directory to place output into. Overrides the standard search order.
-f|--filename filename	The filename for the output. The default filename is the name of the radio. Filename should NOT include any path or extension.
--first n	The First system number to read. / The number specified must be an integer > 0 / System numbers are based on the order in which they are stored in the radio. / Used with Uniden Dynamic Radios only.
--globals	Also get information from the radio on information relating to search and various settings that are not specific to any ‘channel’ / Additional records that are added to the output file will depend on the particular radio.
-i|--irenum x	Renumber channels using ICOM Group channel specification (GGCC). / ‘GG’ is the group number, and ‘CC’ is the channel number. / Group number will be assigned sequentially starting with ‘00’ / ‘x’ is an optional value for the first channel number in each group. / If ‘x’ is omitted, the channel renumber starts at ‘0’. / If ‘x’ is less than 0, all channel numbers will be set to -1 (not used). / If renumbering a group results in a channel number greater than 99, that channel will be set to -1 (not used). / This option should NOT be used if --renum specified.
--keyformat	Output records will be in the form: keyword=value, rather than positional fields. / Note: For trunked systems, the 'freq' records will always be in keyword=value format, as most of the positional fields in this record are not used for these systems.
--nocomment	Do NOT generate ‘freq’ record comments after the end of each set of ‘group’ records .
--nohdr	Do not generate header records. This option will be forced if –append option specified.
--notrunk	Only read conventional systems. / This option is only used for Uniden Dynamic Radios. / All other radios use only conventional systems.
-o	Overwrite any existing file without prompting.
--posformat	All output records will be in positional format (Including Trunked Systems).
-q n	Change all SYSTEM and SITE quick-keys to the number indicated. ‘n’ must be an integer between 0 and 99. / This is used ONLY with Uniden Dynamic Radios.
--renum x	Renumber the channels. ‘x’ is an optional value for the first channel number. / If ‘x’ is omitted, the channel renumber starts at ‘0’. / If ‘x’ is less than 0, all channel numbers will be set to -1 (not used). / This option should NOT be used if --irenum specified.
-s	Sort FREQ records by frequency. If the output only contains Trunked systems, this option is ignored, as FREQ records contain 'TGID's instead of frequencies for these systems.
--search	Also get search channels from the radio. / NOTE: Only functional with Uniden BCD325P2 and BCD396T Radios.
--skip	Skip empty channels. Normally empty channels are saved with a frequency equal to 0.
--toneout	Also get tone-out information from the radio. / NOTE: Only functional with Uniden BCD325P2 and BCD396T Radios.
-z|--Hz	Store frequencies in Hz. The default is in MHz

## HPD2CSV
Inputs: One file specification.

 This will convert .hpd files to RadioCtl .csv files. These can be from the Uniden master database, or from Favorites Lists in the Radio. Only one input file can be processed at a time.
The output file name defaults to the name of the input file (with a .csv file extension). The directory where the output files are placed is determined by the 'tempdir' setting specified in the radioctl.conf file.
NOTE: Converting a large .hpd file can take a bit of time, depending on the options and the processing speed of your computer.

The following options are recognized for the SDS2CSV command:

Table 10: Options for HPD2CSV command
option	description
--append	Append output to any existing file. The default is to replace the contents of any existing file.
--dir directory	Directory to place output into. Overrides the standard selection.
--dqkey	Assign Department quick-keys (if missing). If --force specified, Department quick-keys will ALWAYS be replaced.
-f|filename filename	The filename for the output. The default filename is 'temp'. Filename should NOT include any path or extension.
--force	Force reassignment of all quick-keys for any quick-key option specified (--dqkey, --sqkey, --tqkey or --gqkey)
--gqkey	Assign GROUP quick-keys (if missing). If --force specified, GROUP quick-keys will ALWAYS be replaced.
--keyformat	Output records will be in the form: keyword=value, rather than positional fields.
--lat coord	Specify the latitude for including records. If specified, only records that have a latitude defined, and are within the radius of this latitude will be kept. The coordinate can be in decimal or DMS (DD:MM:SS.SS:direction) format.
--lon coord	Specify the longitude for including records. If specified, only records that have a longitude defined, and are within the radius of this longitude will be kept. The coordinate can be in decimal or DMS (DD:MM:SS.SS:direction) format.
--loc location_name	Name of a pre-defined location in the the configuration file. If specified, this will set the --lat and --lon options to the coordinates defined in this location.
--nohdr	Don't generate header records.
-o|--overwrite	Overwrite any existing file without prompting.
--radius	The radius in miles for the --lat & --lon options. Defaults to 50.
-s|--sort	Sort FREQ records by frequency. If the output only contains Trunked systems, this option is ignored, as FREQ records contain 'TGID's instead of frequencies for these systems.
--sqkey	Assign SYSTEM quick-keys (if missing). If --force specified, SYSTEM quick-keys will ALWAYS be replaced.
--tqkey	Assign SITE quick-keys (if missing). If --force specified, SITE quick-keys will ALWAYS be replaced.
-z|--Hz	Store frequencies in Hz. The default is in MHz

Some notes on quick-key options (--dqkey, --gqkey, --sqkey and --tqkey):

When any of these options are specified, the program will make a ‘best-attempt’ to reduce duplication of various quick-keys. However, some duplication may be unavoidable due to a limited number of quick-key numbers (only 0-99 can be used) or the order in which the files are read. These options are provided to assure that every record that needs it has a quick-key assigned. However, the BEST way to assure the proper assignment is for the user to edit the output file and add the values.

Department quick-keys are used ONLY in the Uniden SDS100 & SDS200 radios. These keys are shared between SITE and GROUP records. To allow these records to be used for other radios (such as the BCD325P2), these records will store Department quick-key values independent of a quick-key value for the record type.

## RADIOS
  Display the names of the currently defined radios. This command has no inputs or options. All radios that are defined to the program will be displayed. The radios listed do NOT have to be connected to the computer to be shown.

## REWRITE
Inputs: One or more file specifications.

 This command will reprocess any number of RadioCtl data files. The output can be a single RadioCtl file, or processed copies of the input files. Each file will be re-indexed, and any options specified applied before being written to.
For a single file, output file name defaults to 'rewrite.csv'. The directory where the output files are placed is determined by the 'tempdir' setting specified in the radioctl.conf file, or by an option on the command line.

Any references to re-indexed records (such as SYSTEM, SITE, or GROUP are preserved as a file is processed. If the output file already exists, the user will be prompted to allow overwriting. The extension of the output file or files is ALWAYS .csv.

Normally, output records are in positional format. However, if the input file records are in keyword=value format, those records will be kept in this format. In addition, TGID records are always generated as keyword=value. These defaults can be overridden with options.

NOTE: Any comments that are NOT part of a :tag structure will be removed in the new file.

The following options are recognized for the REWRITE command:

Table 11: Options for Rewrite command
option	description
--append	Append output to any existing file. The default is to replace the contents of any existing file. This option is ignored if the --keep option is specified.
--dir directory	Directory to place output into. Overrides the standard selection.
--dqkey	Assign Department quick-keys (if missing). If --force specified, Department quick-keys will ALWAYS be replaced.
-f|fname filename	The filename for a single output file. The default filename is 'rewrite'. Filename should NOT include any path or extension. / This option will be ignore if the --keep option is specified.
--force	Force reassignment of all quick-keys for any quick-key option specified (--dqkey, --sqkey, --tqkey or --gqkey)
--gqkey	Assign GROUP quick-keys (if missing). If --force specified, GROUP quick-keys will ALWAYS be replaced.
-i|--irenum x	Renumber channels using ICOM Group channel specification (GGCC). / ‘GG’ is the group number, and ‘CC’ is the channel number. / Group number will be assigned sequentially starting with ‘00’ / ‘x’ is an optional value for the first channel number in each group. / If ‘x’ is omitted, the channel renumber starts at ‘0’. / If ‘x’ is less than 0, all channel numbers will be set to -1 (not used). / If renumbering a group results in a channel number greater than 99, that channel will be set to -1 (not used). / NOTE: ‘Orphaned’ records will have the channel set to -1 (disabled) / This option should NOT be used if --renum specified.
--keep	Keep output names. The output will be in one or more files with the same name as the input file(s). / If this option is NOT specified, a single output file will be generated with the contents of all the input files.
-k|--keyfmt	All output records will be in the form: keyword=value, rather than positional fields.
--nohdr	Don't generate header records.
-o|--owrite	Overwrite any existing file without prompting.
-p|--posfmt	All output records will be in positional format.
--renum x	Renumber the channels. ‘x’ is an optional value for the first channel number. / If ‘x’ is omitted, the channel renumber starts at ‘0’. / If ‘x’ is less than 0, all channel numbers will be set to -1 (not used). / ‘Orphaned’ records will have the channel set to -1 (disabled) / This option should NOT be used if --irenum specified.
-s|--sort	Sort FREQ records by frequency. If the output only contains Trunked systems, this option is ignored, as FREQ records contain 'TGID's instead of frequencies for these systems.
--sqkey	Assign SYSTEM quick-keys (if missing). If --force specified, SYSTEM quick-keys will ALWAYS be replaced.
--tqkey	Assign SITE quick-keys (if missing). If --force specified, SITE quick-keys will ALWAYS be replaced.
-z|--Hz	Store frequencies in Hz. The default is in MHz

Some notes on quick-key options (--dqkey, --gqkey, --sqkey and --tqkey):

When any of these options are specified, the program will make a ‘best-attempt’ to reduce duplication of various quick-keys. However, some duplication may be unavoidable due to a limited number of quick-key numbers (only 0-99 can be used) or the order in which the files are read. These options are provided to assure that every record that needs it has a quick-key assigned. However, the BEST way to assure the proper assignment is for the user to edit each file and add the values.

Department quick-keys are used ONLY in the Uniden SDS100 & SDS200 radios. These keys are shared between SITE and GROUP records. To allow these records to be used for other radios (such as the BCD325P2), these records will store Department quick-key values independent of a quick-key value for the record type.

Quick-keys are ONLY used by Uniden Radios.

## STORE
Inputs: Name of radio for writing (must be specified first).
        RadioCtl file(s).

This command will write memory channels into the radio specified. The first parameter for the command is the name of the radio (from the configuration file). Following the radio name, one or more file specifications must be entered. The files can be RadioCtl type .CSV files, or files containing lists of RadioCtl CSV file specifications. If the first record in the file does NOT start with '*radioctl', then the file will be assumed to be a list of file specs. Unless the files reside in the current directory, the full path needs to be included with every file specified. See the documentation file RadioCtl-Data Files.odt for the file and record format for the input.

How this function operates is dependent on the radio model that is being written.

### BCD325P2/BCD396T
   All of the systems, groups and frequencies included in the input file(s) will be written to the radio's memory. New systems will ALWAYS be generated, Existing systems in the radio will not be modified unless the --erase option is specified. If the radio's dynamic memory gets exhausted, then the operation will terminate.

RadioCtl requires that a SYSTEM quick-key MUST be defined for all Conventional SYSTEM records. Conventional systems that do NOT have a valid quick-key defined will NOT be stored in the radio. For trunked systems, the BCD325P2 does NOT utilize the SYSTEM quick-key, so the program will not required it. Instead, each individual SITE record determines quick-key usage. For the BCD396T, a quick-key is required for ALL system records (trunked or conventional), as this radio does not utilize SITE records.
For Conventional systems, the SYSTEM quick-key will be turned ON if the ‘valid’ field is TRUE, Turned OFF if the valid field is FALSE. However, if the ‘turnqk’ key is defined, then the quick-key will be turned ON or OFF based on the value in this key.

RadioCtl also requires that each SITE record have a quick-key, or it will not be stored. A Trunked system for the BCD325P2 MUST have at least one valid SITE defined, or the system will NOT be stored. Each SITE must have at LEAST one TFREQ record defined or the SITE will be bypassed.
SITE quick-keys are turned ON if the valid field is TRUE, OFF if the valid field is false. However, if the ‘turnqk’ key is defined, then the quick-key will be turned ON or OFF based on the value in this key.
SITE records are not used by the BCD396T.

For GROUP records, a defined quick-key is recommended, but NOT required. If a quick-key IS defined, it will be turned ON if the valid field is TRUE, OFF if the valid field is FALSE. However, if the ‘turnqk’ key is defined, then the quick-key will be turned ON or OFF based on the value in this key.

If a quick-key is NOT defined for a group, a warning message will be displayed, and the group will have ‘LOUT’ (Lock-Out) turned on, as the group cannot be selected/deselected.

The radio makes it hard to select the system if ALL groups are locked-out or all group quick-keys turned off. Because of this, the program will attempt to detect this situation, and modify settings so that at LEAST one group is active.

Any group quick-key that is > 9 will be adjusted by a mod 10 operations.
  EX: quick-key 23 => quick-key 3

The radio only only allows 20 groups per system. The process will terminate after 20 groups are stored.

### SDS200/SDS100
  Because these radios do NOT contain any memory, this operation cannot be executed for these models. Use the CSV2HPD command to convert RadioCtl files to save in the SD Card for these radios.

### ICOM IC-R30
   This radio does not have the ability to store directly. All memory channels must be loaded from the SD Card. Use the CSV2ICOM command to generate this data.
### ICOM IC-705/ICOM IC-R8600
  These radios contain 100 ‘groups’ of 100 channels for each group. Both group and channel addresses are 0-99. The ‘channel’ field in each RadioCtl FREQ record specifies these memory channels as 0-9999, where channels 0-99 are group 0, channels 100-199 are group 1, etc. This is referred to as ‘GGCC’ specification (‘GG’ is group, ‘CC’ is channel in that group).

Each RadioCtl FREQ record will be stored in the channel specified in that record. Channels are expected to be in ‘GGCC’ format.
Ex: If ‘channel’ field is ‘234’, the data will be stored in the Radio’s Group 02, Channel 34.

The RadioCtl GROUP records are usually not used for this operation with a couple of exceptions:

   Both GROUP and FREQ records can specify the ‘scangrp’ key. This key identifies a record as being part of a ‘scanning group’ in the radio. For the IC-705, there are 3 of these (numbered 1-3), while the IC-R8600 has 9. This key is entered as an ‘_extra’ field on positional FREQ or GROUP records in the RadioCtl data file. If this key is specified on a FREQ record, it will be set in the radio for that channel. If it is NOT specified on the FREQ record, but it IS specified on the referenced GROUP record, the value from the GROUP record will be set in the radio.

If the --renum option is specified, the channel number in the FREQ record is ignored. Instead, channels are written to sequentially starting with the first channel in each group (usually 0). Groups are selected incrementally starting with 0 for each GROUP record in the file. If a number is given with the --renum option, the first channel in each group written will be that number.

ex: --renum 5 # the first FREQ record in the file will be written to the Radio’s Group 0, channel 5.

If renumbering causes a channel in a group to be larger than 99, then that record will NOT be stored in the radio.

NOTE:Although these radios can theoretically access 10,000 channels, the storage limit is a LOT lower. The IC-705 can store a maximum of 500 channels. The IC-R8600 can store 2000.

### All other radios
System and Group records are not used. Only frequencies from non-trunked systems in the input file(s) will be stored. The channel number MUST be specified on each 'freq' record to store, and be within the range of the radio's memory Any record with a channel number missing or outside the range will be ignored.
Frequencies must also be within the range of the radio. If the frequency is outside the range, the record is ignored. The exception is if frequency is 0. In this case, the memory channel will be cleared.
Note that some radios (such as the Kenwood TH-F6A) will also adjust frequencies that are not within a particular step value for the frequency.

The following options are recognized for the STORE command:

option	description
--count n	Count of channels to store. The operation will terminate after ‘n’ channels have been successfully stored in the radio. / This option is ignored for Uniden Dynamic Radios.
--erase	For Uniden Dynamic radios, if a system exists with the same 'service' data as the one being written, erase that system before writing the new one. The comparison for the service name IS case sensitive. / This option is not used for all other radios.
--globals	Store any global information records (from the input file) into the Radio.
--nodie	For Uniden radios, do not exit if there are records in error. Normally, if any record has issues, the operation will terminate. / Note that any records with an error (and the children of that record) will NEVER be stored in the radio.
--nosys	Don’t store systems. This is used in conjunction with the --globals and/or --search options when those are the ONLY records that should be set.
--port device	Specify a port (device) to use. Ports are usually /dev/ttyUSBx or /dev/ttyACMx. / If not specified, the program will attempt to automatically locate the correct port. / Normally, this option should not be needed, as the program SHOULD be able to detect where the radio port is.
--renum x	Renumber the channels. ‘x’ is an optional value for the first channel number. If specified, the value must be 0 or greater (negative values are NOT allowed). / If ‘x’ is omitted, the channel renumber starts at ‘0’. / If the radio is an ICOM radio with group support (IC-705/R8600), renumber will use ‘GGCC’ format for the renumbering. / ‘GG’ is the group number, and ‘CC’ is the channel number. / Group number will be assigned sequentially starting with ‘00’, channels for each group will start with the ‘x’ specified, or 0. / NOTE: ‘Orphaned’ records (those that do NOT reference a GROUP/SYSTEM record) will have the channel set to -1 (disabled) / This option is ignored for Dynamic Radios (Uniden).
--search	Store any SEARCH records from the input file into the radio. / NOTE: This is only valid for BCD325P2 and BCD396T radios.
--tone	Store any TONE records from the input file into the radio. / NOTE:This is only valid for BCD324P2 radios.

# File Formats
 File formats are documented in a separate file, RadioCtl-DataFiles.odt